## Slide 1
Quantum Technologies for Neutrino Mass
A collaboration of particle, atomic and solid state physicists, electronics engineers and quantum sensor experts
Cyclotron Radiation Emission Spectroscopy (CRES)
Goal: To build on recent investment in quantum sensors to assess feasibility of an experiment capable of a positive neutrino mass measurement from 3H 𝞫-decay using CRES technology.
Feasibility of e-spectroscopy with CRES demonstrated by Project 8

## Slide 2
QTNM is one of 7 projects funded for 3 years under the UKRI QTFP* Programme
* Quantum Technologies for Fundamental Physics
The aim is to build CRES Demonstration Apparatus, CRESDA, based on Deuterium-atoms but “Tritium-ready”
CRESDA
D/T atomic source
D/T atoms cooling and trapping
D/T atoms as quantum sensors for 3D B-field uniformity mapping at ≤ 0.1ppm
Quantum-limited systems for microwave radiation detection
Trap simulations, CRES signal modelling, Sensitivity and scale-up studies

## Slide 3
CRESDA. Atomic Source and Magnetic Trap.
A number of designs under consideration
1L trap with 𝝆~1012-1014 cm-3.
Initially operate with D-atoms, tritium ready.
Extensive characterisation of trap’s content (density, velocity distributions…)
B-field mapping with ≤ 0.1ppm using D-atoms as quantum sensors
D2 background characterisation

## Slide 4
MW signal
Antennas
SQUID or JTWPA preamp
HEMT amp
CRESDA. Quantum MW-Spectrometer.

## Slide 5: QTNM Future Outlook
A (VERY) tentative timeline
Current project: 2021-2024
  Technology demonstration with Deuterium which is Tritium ready
Next step. 2025-2029
  Moving CRESDA to a Tritium facility (strong engagement with Culham)
  Tritium phase demonstration
  O(eV) sensitivity
”Ultimate” international project > 2029
  Consolidate technological breakthroughs (QTNM, Project-8, …) to build and operate a detector with a phased sensitivity: 100 meV ⇨ 50 meV ⇨ 10 meV plus sterile neutrino programme