SLAC - End Station A
ILC testrun – April '06
Bino Maiheu
University College London
...
Overview, status, results and future plans
Dubna meeting 30-31 May 2006

---
End Station A
Technical drawing of the End Station setup
In the alcove (BPMs 41, 42) (ESA_zlocations1.pdf)
Further downstream: SPEAR girders with BPMs 3,4,5 (new triplet) and BPMs 9,10,11 (ESA_zlocations2.pdf)
Last run :
T474 : energy spectrometer
T480 : wakefield box
Bunch length studies

---
BPMs used :
Old SLAC BPMs, x and y separate
New model, no Q, x and y in same cavity

---
A-Line setup, optics configurations
C455
BPM3, 4, 5
C458
Blow up beam in y
BPM41, 42
BPM9, 10, 11
Configuration with a 'waist' in center of future chicane

---
BPM Data Acquisition, Readout
BPM
2.86 GHz
Downmixed signal
73 MHz
LO
SiS330x Sampling ADC
100 MHz
Ext: 119 MHz
BPM 3,4,5
BPM 9,10,11

---
Amplitude and Phase determination
One way.. fitting the waveforms !
p_{0} e^{-t over p_{1} } sin(p_{2}t + p_{3}) + p_{4}
Extrapolation for saturated signals
However extremely sensitive :
initial frequency of waveform
starting point for fit
Often fails :-(
Practical method : Digital DownConversion (DDC)

---
Amplitude and Phase determination
The other way... DDC
Conversion to baseband by software multiplication with sin wave in timedomain,
Subject to number of input parameters :
filter bandwidth
decay constant of exponential (Q factor)
resonance frequency
starting time of signal (t0)
Determine by hand
Using minimization
Handling of saturated pulses : needs some work !!
Amplitude and Phase : normalization by Q cavity (monopole signal)

---
Default calibration : corrector scans
IQ plots :
Amplitude & Phase
Position & Tilt
Corrector scans to calibrate the
measured positions in BPMs
use 2 correctors in both x and y

---
BPM4 mover calibration
In ILC would be very 'unpopular' to use corrector scan for BPM calibration...
Use BPM4 mover (high precision!) to calibrate BPM4 : both x and y !
Crosscheck existing calibrations
Could be very valuable tool for energy BPMs (all on moving platform...)

---
BPM4 mover calibration
Results e.g. for runs 319-320-321-323-324 :

---
Determining BPM resolution
Problematic !!
1 to 1 correlation as expected

---
Rough BPM resolution : eg. x10Pos
Get rid of beam jitter : correlate positions in different BPMs
Task is now e.g. to understand features like :

---
Singular Value Decomposition
x : vector with correlation coefficients
b : measured position in BPM10x
A . x = b
Matrix A :
ev 1
ev 2
...
1	x9	x11
.	.	.
.	.	.
Same data run (712), using BPMs 9x and 11x

---
Alignment plots : used BPMs 41 & 11
Fairly possible to
stear beam down on all BPMs even though they are not on movers

---
Least square fitting with systematics
Trying to determine the orbit : need some discussion (T474 meeting)
drawing straight line between BPMs 41 and 11 ?
define orbit by BPMs 31,32 and 41,42 ?
Fitting globally, a line ?, a parabola (earth's magnetic field)?
Trying to implement an alternative for SVD:
http://www.phys.ufl.edu/~avery/fitting.html
%chi^{2} = (vec y - A vec %eta )^{T} V^{-1} ( vec y - A vec %eta)
%chi^{2} = sum from{l} (vec y_{l} - A_{l} vec %eta_{l} - B_{l} vec v )^{T} V_{l}^{-1} ( vec y_{l} - A_{l} vec %eta_{l} - B_{l} vec v )
Systematic effects (offsets) you try to get out by collecting multiple fits

---
Online position display in LabVIEW
Apply and tune DDC algorithm in LabVIEW, and hope it's fast enough ;-)
Integrate calibration information
Ship as subvi to DAQ computer for July test run
Raw waveform
Online integration of the calibration
FFT

---
Data processing
Large amount of runs taken :
stability runs, calibration runs
different beam optics configurations
external and internal clocking
Copied to UCL
NEED :
Determine optimised parameters (filtBW, gamma, freq,...)
for DDC algorithm on BPMs 3,4,5
Go over all calibrations manually and redo
(check stability, think of automation)
Reprocess runs

---
Next few weeks
Agree upon default data quality, selection criteria, orbit definition (meeting) :
encoded in libRooEsa
Start systematic studies : run conditions in runlist : resolution stability versus :
Temperature (ambient, thermocouple,...)
Beam energy
Bunch charge and shape
Internal vs. external clocking
Effect of beam optics configuration
Check calibration stability, seek out factors that influence calibration...
Endgoal for data analysis should be a report describing in detail the collective
studies done during this testrun and come up with a plan for
the July running !!
Long term stability runs : 8-hrs shift : calib – stability – calib - stability...
Actively study effect of temperature ...
FONT plans to install a mess up the beam --> study effect on BPM resolution...

---
Discussion, phoneconf. preparation
What needs to be done in for the next years of testrunning
Refurbishement of magnets (at SLAC)
Setup for measurements for magnets : readout, control (power supply)
Think of how accurately magnets need to be measured ?
Do we need to monitor continuously ? + which probes/method ? + how accurate ?
What is available (SLAC, Dubna ?) (possible to transport ?)
Magnet installation
Magnet specifications from old SLAC magnet --> Dubna simulation
What is sergei's code doing, using TOSCA simulation of magnets ? Calculation of effect of imperfections on beam optics ??
What kind of effects can TOSCA simulate ? + how accurate ?
How do we split the tasks, who is doing what ?
What equipment is needed, what is available ??
Should come up with a list !!! + assign people to that list
If stuff needs to bought, where does the money come from ?