simpleSpectrometer
and some Geant4 insights :s
Bino
BPM spectrometer meeting
16 november 2006
UCL

---
spectrometerDipoleFieldMap
Loads a fieldmap file, format :
# Dubna Fieldmap - N. Morozon, S. Kostromin
# Simulation of 10D37 magnet using TOSCA (N. Morozov)
# All positions are in mm, (z,x) = (0,0) is center of magnet
# Magnetic field values are in Gauss
# z(mm) B(x=0mm) B(x=5mm) B(x=10 ) B(x=15 ) B(x=20 ) B(x=25 ) B(x=30 ) B(x=35m) B(x=40 )
* 0.0 5.0 10.0 15.0 20.0 25.0 30.0 35.0 40.0
   0.0 1125.36 1125.36 1125.39 1125.42 1125.47 1125.54 1125.61 1125.69 1125.78
  10.0 1125.35 1125.36 1125.38 1125.42 1125.47 1125.53 1125.60 1125.69 1125.77
...
Dynamic ( using std::vector<double> ) so no need to specify size in the file, just need to know
the x-positions for each z position... hence the “*”- line, characterizing the x positions..
Fieldmap specified only for a quadrant of the magnet... -z and -x are mirrored...
Does this need to be more general ??
Interpolation
Define closest 3x3 square, do first 3 parabolic interpolations ( 3 points = 1 parabola ) in z
direction ( more points... ) and then 1 parabolic interpolation in x
Implements the spectrometerDipoleFieldMap::GetFieldValue( ) as a concrete
implementation of the pure virtual function in the abstract G4MagneticField class
from which it is derived
GetFieldValue( const G4double Point[4], G4double *Bfield )
Point[ x, y, z, time ]
Returns Bfield[ x, y, z ]

---
Currently little hack to get to local coordinates in the dipole volume as the
GetFieldValue() routine gets queried with the global coordinates
Know how to do it properly ( see BDSIM ), just have to do it :)
Sometimes the stepper queries the fieldmap with extreme positions, set field to 0
outside of the boundaries of the field ( no extrapolation...)
SpectrometerMaterials
Problem of defining vacuum :
No real vacuum exists, vacuum is just low density air :)
Get G4_AIR from NIST database ( implemented in Geant ) : G4NistManager
Set temperature ( 300 K ) and pressure e.g. ( 1.e-9 mbar ) and calculate density using
ideal gas law & molar mass of air ( ~29 g/mol )
construct vacuum :
spec_Vacuum = new G4Material( "spec_Vacuum", dens, 1, kStateGas, temp, press );
spec_Vacuum->AddMaterial( spec_Air, 1. ); // ... a vacuum of air :)
All materials will be in spectrometerMaterials
Global extern spectrometerMaterials* gMat; object, instantiated
at top of spectrometerMaterials.cc

---
SpectrometerOutput & the hits collection
At end of event, a hits collection is available in Geant, so need to derive a concrete class
, spectrometerUserEventAction, from G4UserEventAction that implements
spectrometerUserEventAction::BeginOfEventAction( const G4Event * );
spectrometerUserEventAction::EndOfEventAction( const G4Event * );
Implement EndOfEventAction to do something with each hits collection, like e.g. Dump to output
  // get the hits collections of this event
  G4HCofThisEvent* hce = evt->GetHCofThisEvent();
  // get the digit collections of this event
  //G4DCofThisEvent* dc = evt->GetDCofThisEvent();
  if ( ! hce ) {
    G4cerr << "*** unable to retrieve hits collections in event " << evt->GetEventID()
        << std::endl;
    return;
  }
  // for each hit collection ( so each sensitive detector ), we dump the hits to the
  // output
  spectrometerBpmHitCollection *bpmHC;
  spectrometerBpmHit *bpmHit;
  for ( G4int i = 0; i < hce->GetNumberOfCollections(); i++ ) {
    bpmHC = ( spectrometerBpmHitCollection* ) hce->GetHC( i );
    for ( G4int j = 0; j < bpmHC->entries(); j++ ) {
      G4cout << " - Hit collection " << i << " contains " << bpmHC->entries()
        << " entr" << (bpmHC->entries() > 1 ? "ies" : "y" ) << " : " << std::endl;
      bpmHit = (*bpmHC)[j];
    } /* end of loop over the hits in one collection */
Each sensitive detector ( BPM in this case ) has a hits collection !!
Can do something here with the hit
So we can plug here also a routine that takes the events hce and spits to whatever

---
The filling of the hits collections happens for each SD in the ProcessHits routine, and
the EndOfEvent routine ( see spectrometerBpmSD::ProcessHits(...)
  /**
     Let's store the hit, so construct a spectrometerBpmHit...
  */
  G4String BpmName = hitCollectionName + "Hit";
  spectrometerBpmHit *bpmHit = new spectrometerBpmHit( BpmName, x, y, z,
        xPrime, yPrime, pdgType, id );
  // insert the hit into the collection
  bpmCollection->insert( bpmHit );
and spectrometerBpmSD::EndOfEvent(...) :
G4SDManager *SDman = G4SDManager::GetSDMpointer();
G4int HCID = SDman->GetCollectionID( hitCollectionName );
HCE->AddHitsCollection( HCID, bpmCollection );
So just would need then a global gOuput pointer which gets pointed to the current output
object ( corresponding with a file ) for each run that gets created and destroyed at beginning
and end of a run (spectrometerUserRunAction) and that has a routine
   gOuput->WriteHits( G4HCofThisEvent *hce )
that gets called at each spectrometerUserEventAction::EndOfEvent( ... )

---
SpectrometerConfiguration
Based on tinyXML loader, example config file : proposal !!! :
<?xml version="1.0" encoding="ISO-8859-1"?>
<!-- Energy spectrometer simulation configuration file -->
<spectrometer>
  <simulation>
    <author>Bino</author>
    <comment>This is just an example...</comment>
    <runs>10</runs>
    <events>100000</events>
  </simulation>
  <beam>
    <energy>28.5</energy>
    <particle>e-</particle>
  </beam>
  <optics> ... </optics>
  <components>
    <bpm name="BPM1" xpos="0." ypos="0." zpos="10.">
       <adcbits>14</adcbits>
    </bpm>
    <dipole name="M1" xpos="0." ypos="0." zpos="10.">
      <length>3.</length>
      <sign>1</sign>
      <fieldmap>10D37.MAP</fieldmap>
    </dipole>
    <bpm name="BPM1" xpos="0." ypos="0." zpos="5.">
      <adcbits>12</adcbits>
    </bpm>
  </components>
</spectrometer>
<!-- ....ooooOOOO0000 "This is the end" 0000OOOOoooo.... -->
category
variable
Specify components with mandatory
attributes --> can generate error
upon missing attribute
all other options can have default
values...

---
Example code :
spectrometerConfig* cnf = new spectrometerConfig();
cnf->Load( "spectrometer.xml" );
double ebeam, betx;
int runs;
string particle;
cnf->Get( "beam", "energy", &ebeam );
cnf->Get( "beam", "particle", &particle );
cnf->Get( "simulation", "runs", &runs );
cnf->Get( "optics", "betx", &(betx) );
cout << "energy = " << ebeam << endl;
cout << "runs = " << runs << endl;
cout << "particle = |" << particle << "|" << endl;
Never store values in real member
variables of the config object : most
flexible.
You define a new xml tag, and it is
immediately available in program...
Get( category, name, <type> *variable )
Overloading a “Get” function in the config class that each time queries the XML DOM
which is read in from the xml file upon creation of the object :
_dom = new TiXmlDocument( xmlfile );
_dom->LoadFile();
Private member of spectrometerConfiguration class
Need to instantiate a global spectrometerConfiguration object upon starting the program...

---
Need to think about the components... maybe store them in the configuration
object as
std::vector<spectrometerBpmConfig>
std::vector<spectrometerDipoleConfig>
where spectrometerBpmConfig and spectrometerDipoleConfig are then
classes that represent the configuration of 1 BPM or 1 dipole magnet...
What else...
Implement somehow beampipe
think of stuff tomorrow... brain doesn't cooperate anymore....

---
In summary... we can bend the beam using the fieldmap and obtain more or less the same
deflection as Sergei's simulation...