BPM Energy Spectrometry
for the International Linear Collider
Bino Maiheu
for Alex, Stew, Fil, Steve, Matthew & David
UCL – HEP group meeting
29 September 2006
UCL HEP Groupmeeting, 29 September 2006 – Bino Maiheu
BPM
BPM
BPM

---
What is the ?
http://www.linearcollider.org
1 TeV
e+
e-
~ 10 km
Proposed ~30 km long linear e+e- collider
CM energy up to 1 TeV
International... obviously
targeted completion around 2020
complementary
However... we're not 2020 yet...
costs ~ PRF
ΔEturn ~ E4 / ρ2

---
ILC layout & challenges
Accelerating gradient ~ 35-40 MeV/m
Damping rings, sources, final focus
Lumi ~ frep / σxσy
frep = 40 kHz (LEP), = 5 Hz (ILC)
-> beam size ~ 1000 times smaller
Test facilities !!
Civil engineering, ....
Beam Delivery System : you only get 1 go !!!
UK has leading role
Beam energy measurement
High quality physics need accuracy ( see later )
No averaging over bunches possible
Min. impact on the beam and physics datataking
OUTDATED

---
Importance of energy measurement
Introducing... Filimon, our one leg in “proper” physics :-) ...
Study of top quark important for standard
model / SUSY constraints
Top quark : large decay width -> pQCD
ILC = top quark factory, QCD precision tests
Top pair production cross section : TOPPIK
Filimon is developing MC generator
for top quark production
based upon TOPPIK
some “voodoo” to improve speed
ILC workshops Vancouver & Valencia
A. Hoang & T. Teubner
F. Gournaris
However... not full story...

---
Influence of beam energy...
GDE stresses importance of link between accelerator physics & particle physics
Top quark mass scan
Luminosity spectrum
Uncertainty on beam energy measurement
contributes directly to the uncertainty on the
ILC physics output...
Importance of top quark ... (see ambleside talks)
Easy, fil/stew's plots... luminosity spectrum... etc..
Monte Carlo.. Teubner.. put filimon in spotlight
[Speaker Notes: - when you do t mass scan, you want to understand the systematics involved in the energy measurement --> direct translation in the mass scan -]

---
BPM Spectrometry
E ~ ∫B.dl/Θ
Study & design magnetic chicane for beam energy measurement using
Beam Position Monitors (BPMs)
Royal Holloway University London: S. Boogert
Cambridge : M. Slater, M. Thomson and D. Ward
University College London: F. Gournaris, A. Lyapin, B. Maiheu, S. Malton, D. Miller and M. Wing
(putting the I in ILC :)
δE/E ~ 10-4
At least δx~ 500 nm needed
Move beam by 5 mm at center
NanoBPM@ATF (KEK) : test resolution, try different analysis methods, BPM stability tests, multi bunch operation, advanced electronics techniques, inclination of beam in BPMs.
-> spectrometer aspects of BPMs can be tested
ESA@SLAC : test stability and operational issues with a full implementation of 4 magnet chicane and 3 BPM stations
-> test of real chicane prototype
BPM
BPM
BPM

---
NanoBPM at ATF (KEK)
BINP BPMs in LLNL/SLAC
spaceframe on hexapods
Collaboration with LBNL, LLNL, SLAC, KEK
KEK BPMs
16 nm resolution achieved !

---
ESA at SLAC (as seen by GoogleEarth)
San Francisco (Hwy 280)
End Station A
2 mile LINAC

---
T474/T491 - ESA@SLAC
Collaboration with LBNL (Y. Kolomensky et al.), SLAC (M. Woods et al.) and Notre Dame (M. Hildreth et al.)
Dipole magnets
BPMs 9,10,11
BPMs 3,4,5
SPEAR girder
20 m
January test run 2006 (4 days) : Commissioning of BPMs 31,32 and 1,2 upstream
April run 2006 ( 2 weeks ) :
Commissioning of new cold linac prototype triplet (BPM 3,4,5), where BPM4 on x,y mover system
Commissioning of old SLAC BPMs (9,10,11)
Digitisation/signal processing optimization
July run 2006 (2 weeks ) :
Commissioning of interferometer system (BPMs 3,4,5) + energy BPM24 upstream
Further optimisation of hardware
Stability data taking with 10 BPMs, frequent calibrations
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
The setup in the End Station
Notre Dame Interferometer
system (M. Hildreth)
New prototype cavities
~ 700 nm in new cold LINAC
prototype cavities, designed by
Z. Li & C. Adolphsen
~ 350 nm in old SLAC cavities
Systematics under investigation
Improving calibration routine
Old SLAC cavities

---
How do these BPMs work... nutshell-ish ?
RF
Filters,
Amplifiers
Filters,
Amplifiers
ADC
+
+
+
+
+
+
+
+
LO
LO
Monopole (TM010) : charge
Dipole (TM110) : charge + offset + tilt
Determine Amplitude & Phase
Fit waveform : V = V0 + A e-Г(t-t0) sin[ω(t-t0) + φ]
Digital Down Conversion (DDC) :
Multiply waveform with eiωt
Filter out 2ω component
Sample waveform -> A, φ
Complex plane
Tilt axis
IQ phase
Disentangle charge, offset and tilt :
1. Normalize signal to Ref (Q) Cavity
2. IQ rotation (π/2 tilt phase difference)
3. Calibrate
Pos. axis
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
Our own spectrometer BPM prototype
Existing BPM designs not optimal for an energy spectrometer
aperture ( machine protection, resolution )
resolution, stability
monopole rejection
coupling -> decay time ( multi bunch )
Take know-how gained from collaborating
with others and design BPM of our own,
suitable for energy spectrometer
Al prototype by UCL workshop
Cu vacuum beam MSSL
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
Spectrometer simulation
Impact of the chicane on the optics of the beam ?
Where does the synchrotron radiation go ?
General opertional issues...
Emittance growth, energy bandwidth of system ?
...
BDSIM
Simulation in GEANT4, BDSIM and MAD
Developing core, platform independent
library for BPM analysis & simulation
GEANT 4 chicane
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
Future plans
Continue to develop Top Monte Carlo generator
Further contributions to NanoBPM & ESA work : spectrometer related studies,
data-analysis...
Commission BPM vacuum prototype in January in ESA beam line and
develop full triplet the coming years...
Simulation work : full simulation of chicane, BPMs, digitization and analysis
And in the end...
Go to GDE and say :
“Look guys, here's a 'little' spreadsheet with
what you need for a BPM spectrometer,
this is how you build it, these are the
systematics involved and this is how it's
measurements will impact the physics
output of the ILC.”
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
Possible PhD projects...
Physics analysis
Other thresholds e.g. SUSY, W+W-, Higgs,...
Energy measurement essential for all of these !
BPM spectrometer
UCL developing BPM triplet system
Plenty of opportunities : electronics, simulations,
data-analysis, beam tests
Linear Collider
Integration of spectrometer into beam delivery system
Exposure to advanced beam instrumentation
Real hardware experience
Accelerator being designed now, PhDs on this project can
Significantly influence design & operation
UCL Groupmeeting, 29 September 2006 – Bino Maiheu

---
Thank you :-)
http://www.hep.ucl.ac.uk/lc/
http://www.hep.ucl.ac.uk/~bino/T474/
http://www.hep.ucl.ac.uk/~liapine/
http://www.hep.ucl.ac.uk/~sboogert/
UCL Groupmeeting, 29 September 2006 – Bino Maiheu