WP 4.2 review meeting
Status of the ESA work...
bino@hep.ucl.ac.uk
Wednesday, 13 September 2006, UCL, bino@hep.ucl.ac.uk

---
Introduction, Overview of the completed runs
January testrun :
- commissioning of BPMs 31,31 and 1,2 (41,42)
- readout, processing software etc...
April run :
- commissioning Chris' BPMs + x,y mover system on BPM4 + BPMs 9-11
- code optimisation, external/internal clocking
July run :
- commissioning of interferometer
- optimisation of hardware (new LO frequency)
- stability data taking interleaved with frequent calibrations

---
“The data” : improvements, optimisations
Spent much time digging in the code, determining optimal DDC constants for ext. (119 MHz) /int. (100MHz) clock to get good resolution !! (after april run)
Tune: t0, t0Ref, filtBW, Gamma, Omega for each BPM
Roughly go from 50 micon resolution to around 5 micron

---
“The data” : improvements, optimisations
During july run :
change in LO frequency
(now mix down to -83 MHz)
Phase dependence of resolution
Down down < 1 micron resolution

---
“The Data” : resolution, stability so far
Drift of the position in BPM9 vs BPM10
Resolution 'out of the box' : BPM 3-5: ~ 700 nm in x, BPM 9-11: ~350 nm in x
20k pulses ~ 30 min

---
Further improvements to algorithm/ROOT files
Need to
Include timing information for the runs ( maybe pulse time stamp or something ) now : external run list with UNIX times for start of run
Implement a second filter to get completely rid of 2 omega component, but need to check whether DDC handles this correctly + need to optimise filter bandwidth for that + recalibrate data
At some point in future... base
processing on our own libespec
Better filter ?
Direct interface with labVIEW online processing etc...
We know the code :)

---
Calibrations
Corrector scans / setpoint calibration... lot of manual work needed
BPMCALI macro
automatic execution with delay between n cycles of corrector scan with feedback + mover scan on BPM4
set voltage level for each step in ADC
still need to implement automatic processing

---
Calibrations, stability
IQ phase and scale stability for July run
e.g. BPM9-11 (>1460)
BPMCALI, scales and IQ phases stable to within a couple of %
However need to understand
the different systematics involved
-> strong case for planned calibtone
Cross check with mover calibration + interferometer
--> think + implement a scheme which corrects automatically the scales using movers + zygo when processing the BPMCALI macro
--> check accuracy of BPMCALI against mover calib

---
Interferometer, Geophone measurements
Data from interferometer on BPM3-5
BPM3 and BPM5 show similar
behaviour
BPM4 (on mover frame) different
frame prob acts as amplifier for
ground vibration
Girders show 20Hz vibration...
Geophone measurements on Girder (Mahsa)
Can we damp this vibration ?
For BPM3-5 in first order we prob. care less then for new BPM frame. Might be
worth is to do FEA on the new support (after figuring out how to do this obviously ;-))

---
Magnet mapping/installation in ESA
As Ray mentioned: use 10D37 magnets
Mike tells me that concrete plans should crystalize within 2-3 weeks for mapping B(x,y,z) and B.dl(x,y)
Ray has started designing Al stands for magnet
Mike has had some discussion with Juergen/Dubna
We need to figure out with Ray what to measure in workshop / in situ
Need concrete plans on distributions of NMR/Hall/Flux Gate magnetometers
Control, feedback etc... need work on that !
Simulations by N. Morozov (Dubna) :
Required Bdl of 0.118 Tm, current needed for that 146 A
Effective length 106.8 m
Expected Bdl uniformity 10-4 in +/- 15mm
Studies on fringe field contributions
Defined region for possible NMR probes
Temperature factor for field integral 6.1 10-5 / C

---
Next ESA run issues
Need people at SLAC for big part of January to prepare
Installing our BPM, readout, temperature, movers etc...
Calibration tone electronics...
Setup processing before the run so can be done more efficient
Might make sense to have someone there for a couple of weeks before end of the year to facilitate communication (maybe help with magnets), and smooth the way for January
Interferometer, link stations using an invar “ruler” as base with interferometer heads at the endpoints. Mike H. is working/thinking about that...
Plans to move BPM4 to middle of the chicane.....
Mike would contact Chris. A on this point
Need to carefully think/discuss about that
Mover range of system (2”... so prob fine)
Design support frame ? Integrate with our own support ???
Preliminary 2007 run dates :
Run 3 : Jan 30 – Feb 12
T-LCLS : July 5 – July 8
Run 4 : July 9 – July 22

---
SLAC Funding
ESA as an ILC facility in the future
Collaboration with DESY/Dubna
Funding for 2007 (FY07) looks good, we will have runs in Jan and Jul 2007.
Funding for 2008 (FY08) doesn't look so good....
Proposal submitted to bring LCLS beam to ESA (T-LCLS, Mike)
need to come up with “ammunition” for Mike to push for funding
targeted NIM paper should be completed by the end of the year !!!
Thought that crossed my mind... how to we see collaboration in future
with DESY/Dubna ? Take some more initiative ourselves there ???