BPM Energy spectrometry,
status & future plans at ESA in SLAC
Bino Maiheu
University College London
Yerevan Collaboration Meeting
23-27 October 2006
Yerevan Collaboration Meeting, 23-18 Oct. 2006 – Bino Maiheu

---
Outline
Principles of BPM based energy measurement
T474/T491 (T474-X) in the End Station A at SLAC
BPM systems deployed and commissioned
Automated BPM calibration
Some systematics, resolution, stability and variations
Interferometer
Our own spectrometer BPM prototype
Simulation & modeling work
Future plans
Yerevan Collaboration Meeting, 23-18 Oct. 2006 – Bino Maiheu

---
BPM based beam energy measurement
Study & design magnetic chicane for beam energy measurement using BPMs
for a future linear collider
E ~ ∫B.dl/Θ
δE/E ~ 10-4
η ~ 5 mm at center
At least δx~ 500 nm needed
NanoBPM@ATF : test resolution, try different analysis methods, BPM stability tests, multi bunch operation, advanced electronics techniques, inclination of beam in BPMs.
-> spectrometer aspects of BPMs can be tested
ESA@SLAC : test stability and operational issues with a full implementation of 4 magnet chicane and 3 BPM stations
-> test of chicane prototype
capable of producing ILC-type bunch
good test bed for systematic studies : vary energy spread, bunch length, beam halo, optics etc...
Yerevan Collaboration Meeting, 23-17 Oct. 2006 – Bino Maiheu
BPM
BPM
BPM

---
ESA at SLAC (GoogleEarth)
San Francisco (Hwy 280)
End Station A
2 mile LINAC
UCL HEP Groupmeeting, 29 September 2006 – Bino Maiheu

---
T474/T491 - ESA@SLAC
Collaboration with LBNL (Y. Kolomensky et al.), SLAC (M. Woods et al.) and Notre Dame (M. Hildreth et al.)
Dipole magnets
BPMs 9,10,11
BPMs 3,4,5
SPEAR girder
20 m
January test run 2006 (4 days) : Commissioning of BPMs 31,32 and 1,2 upstream
April run 2006 ( 2 weeks ) :
Commissioning of new ILC prototype linac triplet (BPM 3,4,5), where BPM4 on x,y mover system
Commissioning of old SLAC BPMs (9,10,11)
Digitisation/signal processing optimization
July run 2006 (2 weeks ) :
Commissioning of Zygo interferometer system (BPMs 3,4,5) + energy BPM24 upstream
Further optimisation of hardware (down mixing)
Stability data taking with 10 BPMs, frequent calibrations
Yerevan Collaboration Meeting, 23-27 Oct. 2006 – Bino Maiheu

---
BPM systems used in ESA
Rectangular cavities
x and y separated
2.856 GHz, high Q ~ 3000
20 mm aperture (0.8 “)
C. Adolphsen, Z. Li
ILC cold linac prototype
cavities
36 mm aperture, 2.859 GHz
low Q (~ 500)
good monopole suppression

---
BPM signal processing in a nutshell
RF
Filters,
Amplifiers
Filters,
Amplifiers
ADC
LO
LO
Monopole (TM010) : charge
Dipole (TM110) : charge + offset + tilt
Determine Amplitude & Phase
Fit waveform : V = V0 + A e-Г(t-t0) sin[ω(t-t0) + φ]
Digital Down Conversion (DDC) :
Multiply waveform with eiωt
Filter out 2ω component
Sample waveform at fixed t0Ref -> A, φ
Tilt axis
IQ phase
Disentangle charge, offset and tilt :
Normalise signal to Ref (Q) Cavity
Pos. axis
Tilt has π/2 phase difference to position
Yerevan Collaboration Meeting, 23-17 Oct. 2006 – Bino Maiheu

---
Automatic calibration
Corrector scans / set point calibration... lot of manual work needed
Automatic setting of correctors with/without
feedback
Followed by mover scan on BPM4
Set voltage level for each step in ADC
Still need to implement automatic processing
Important aspect of future
spectrometer operation !

---
Phase systematics
Resolution data from April run showed strong
Q phase dependence
Problem traced back to non-perfect filtering of
2ω peak +
separation between sampling and downmixed
frequencies (reflection from upper nyquist
band)
Hardware solution : encrease LO by 10 MHz

---
Phase systematics, new LO frequency
Better separated !
Effect on resolution :

---
ESA Resolution & stability
old cavities
200 nm
Resolution : BPM 3-5: ~ 700 nm in x, BPM 9-11: ~350 nm in x
20k pulses ~ 30 min
prototype

---
Some long term stability results
In a flash :)

---
Some long term stability results
In a flash :)
Need more work !
Seeing some interesting effects,
understand electronics better !

---
Interferometer
M. Hildreth, M. Albrecht (Notre Dame)
commissioned during July run
sub nm resolution
stability of < 30 nm (1 hr) with fixed mirror
plan to link BPM stations

---
Interferometer
M. Hildreth, M. Albrecht (Notre Dame)
commissioned during July run
sub nm resolution
stability of < 30 nm (1 hr) with fixed mirror
plan to link BPM stations

---
Spectrometer BPM prototype
Existing BPM designs not optimal for an energy spectrometer
aperture ( machine protection, resolution )
resolution, stability
monopole rejection ( electric center stability )
coupling -> decay time ( multi bunch )
Al prototype
Designed new prototype (A. Lyapin)
30 mm aperture, 2.878 GHz, 1.3 MHz bandwidth
theoretical resolution ~ 11.2 nm
Al prototype by UCL workshop, Cu vacuum beam
prototype by Mullard Space Science Lab (MSSL)
Proposed electronics scheme

---
Aluminium prototype for new BPM
Waveguide structure
Alex
Front face
Cavity (upside down)
Al prototype is done & ready for measurements at UCL & RHUL
Fully assembled prototype
Feed through

---
Chicane simulation
Currently most simulation work just
generates “sampled waveforms”
Developing core library for full simulation :
Uses physical units ( easily portable between e.g.
KEK & SLAC )
Portability between platforms, e.g. import into LabVIEW
Simulation of electronics : loss, non linearity, digitization
Contains analysis routines as well -> simulation & real data
analysis based upon idential set of routines
Real
BPM
reconstruction
analysis
Electronics
digitisation
Chicane
simulation
GEANT/BDSIM
Waveform
simulation
Electronics
digitization
simulation
First implementation :
GEANT 4
BDSIM
cavity
parameter
simulation
Already contains a lot of functionality
cross check with ESA data
production underway
(GdfidL)
libespec

---
Closing remarks & future plans
Plans for ESA :
Install 4 magnets in beam line (Jan. '07)
Install & commission new spectrometer BPM prototype
complete with temperature readout and x,y mover system
Commission constant calibration tone system to monitor gain drifts
in electronics
Link BPM stations with interferometer system (M. Hildreth)