## Slide 1: UCL Proton Therapy Calorimetry Group Meeting 17.06.2016
Anastasia Basharina-Freshville
(University College London)

## Slide 2
General Updates (1)
Work on-going to write a waveform reader and fitter:
  Reader: complete
    Automatically calculates the number of points per event (this is a setting on the digitiser and can vary for runs)
    Creates a tree with a histogram for each waveform
  Fitter: in progress
    Next steps: Fit the decay time with an exponential, extract parameters and combine all three parts
    Create a tree with variables such as the chi^2 of the overall fit and values of the rise and decay times etc.
1. pol0 + gaus (rise time)
2. 1/gaus (peak)
3. Extract parameters from 1 and 2 and combine
?

## Slide 3
General Updates (2)
Next Clatterbridge test beam:
  2nd and 3rd of August
  Prepare for energy-range calibration measurement (coordinate with Adnrzej and the Clatterbridge team)
  Acquire more low and high rate waveform data to train our waveform fitters
  Acquire data with new oscilloscope
  During all measurements monitor the dose “delivered” to the scintillator to monitor any radiation damage to the scintillator
  Other tests to consider:
    Use a fresh scintillator for radiation hardness tests (MUST be done at some point)
    Look at the spatial uniformity of the beam with a collimator with an off-axis hole
LED light injection system ready to be tested
  Currently uses SuperNEMO BIVAR 400 nm LED
  Order VAOL-5GUV8T4 380 nm LEDs made by VCC
    Tested by SuperNEMO colleagues in Texas: good illumination uniformity and consistent from one LED to the next
Proton Therapy Calorimetry seminar at University of Sussex on the 17th of November 2016

## Slide 4
Portable HV Unit Pedestal (1)
During 207Bi measurements I noticed a wider than usual non-Gaussian pedestal when using the portable HV unit
  It contributes to the width of the energy resolution measurement with 207Bi
  Currently we only subtratct the mean of the pedestal but not its width
“Healthy” looking pedestal when using UCL HV crate:
v

## Slide 5
Portable HV Unit Pedestal (2)
Already tried:
  Swapping HV cable
  Swapping channels on portable HV unit
  Swapping the power cable for the HV unit (just in case!)
  To no avail…
Now:
  “Filtering” plug in D29
  3 m long grounding braid: copper braid surrounded by steel, from the portable HV unit to the DAQ used to acquire the 207Bi data

## Slide 6
Portable HV Unit Pedestal (3)
?

## Slide 7
Portable HV Unit Pedestal (4)
Next:
  Ensure grounding is set up correctly
  Acquire data with our digitiser to see whether the widening in the distribution is still there
?