## Slide 1
LeCroyRoutines.C
LeCroyData class (loading .trc files)
LeCroySpectrum class (generating spectra)

## Slide 2: LeCroyData
Instantiation: new LeCroyData(std::string fileName);
Recommend using ‘new’ for compatibility with LeCroySpectrum class.
fileName must identify a file ending in ‘.trc’, located relative to the working directory.

## Slide 3: LeCroyData
getWaveArray();
  Returns a c-style array of doubles: every voltage reading loaded from the file, sequentially.
getTimeArray();
  Returns a c-style array of doubles: each time point loaded from file, sequentially, with zero at the first trigger in the file.

## Slide 4: LeCroyData
getAcqWave(int i);
  Returns a c-style array of doubles: every voltage reading from the ith acquisition window, sequentially.
getAcqTime(int i);
  Returns a c-style array of doubles: each time point from the ith acquisition window, sequentially, with zero at the trigger time for that acquisition.

## Slide 5: LeCroyData
getAcqCount();
  Returns long: the number of acquisition windows recorded in the file.
getPointsPerAcq();
  Returns an int: the number of points recorded in each acquisition window.

## Slide 6: LeCroyData
getTriggerArray();
  Returns a c-style array of doubles: The number of ms past the first trigger in the file at which each trigger occurs.
getOffsetArray();
  Returns a c-style array of doubles: The time in ms recorded before a trigger for each trigger in the file.

## Slide 7: LeCroyData
getTimestamp(); - A string representing when the file was created
getHeader(); - A string containing mostly diagnostic information
getInstrumentName();
getInstrumentNumber();
getTraceLabel();

## Slide 8: LeCroySpectrum
This class will probably continue to be updated!
Constructor takes a pointer to a LeCroyData object.

## Slide 9: LeCroySpectrum
getSpectrumArray();
  Returns a C-style array of doubles, each corresponding to the integrated ADC counts found for one waveform. Values are reported in mV ns.
getTimeArray();
  Returns a C-style array of doubles, each corresponding to the time at which a waveform contributing to the spectrum was found. Values are reported in ns relative to the first trigger in the file.
  The waveform with ADC counts given by getSpectrumArray()[i] started at a time getTimeArray()[i].
getArraySize();
  Returns the number of elements in the spectrum array as an integer.

## Slide 10: LeCroySpectrum
setRise(double level);
  Sets the value in mV above which a signal must rise for a waveform to be registered. Default is 30. mV.
setFall(double level);
  Sets the value in mV below which a signal must fall for a waveform to be considered ended. Default is 20. mV.
setBaselineSigmaLimit(double level);
  Sets the maximum allowed standard deviation of the pre-trigger region of an acquisition. Default is 20. mV.
setData(LeCroyData* lcd);
  Sets the data under consideration by the LeCroySpectrum object to be that contained within lcd.

## Slide 11: LeCroySpectrum
Performance warning:
  At the moment, each of the setX(double) methods causes the spectrum array and time array to be recalculated. This is to ensure that the values reported by the getX() methods are consistent with the state of the LeCroySpectrum object. In the interactive setting, the slowdown is almost imperceptible, but making many changes to the internal state in, for example, a very long loop, might become slow!

## Slide 12: LeCroySpectrum
printToFile(std::string fileName);
  Writes the information contained within the LeCroySpectrum object to a file with name fileName. Current format is three comment lines, starting with #.
  First comment line: Date and time at which data was collected
  Second line: Number of points in the spectrum reported
  Third line: The internal state of the LeCroySpectrum object (rise, fall, and sigma limit levels) at the time the file was written.
  The ith line after the comment lines contains: getTimeArray()[i] getSpectrumArray()[i] Where the separation is a tab.