Analysis: Crosstalk and Birks constant

---
Crosstalk
PMMA degrader (8 x 7mm)
PMMA
Scintillator
Scintillator

---
Scintillator
PMMA degrader
PMMA
Scintillator
Crosstalk+misalignment?

---
If the total light output in the PMMA within 2mm distance is counted, it contributes 7% of the normalised light output.
This is misleading because a large chunk of this comes from the sheet standing at an angle (misalignment)
In addition, the light calibration image has the same crosstalk&misalignment. So does light calibration correct for crosstalk and misalignment?
Problem: What if the light output between two sheets is very different, i.e. in/behind the Bragg peak?
Mitigation technique: I reject the light output from the edges of each sheet (0.5mm) because light spikes tend to appear there. I assume they stem from small alignment changes but can also be caused by crosstalk.

---
Birks’ constant
Birks constant is an unknown material constant
Use quenched Bragg model to fit data and measure Birks
Best fit is used as constant parameter for later fits
Problem: Different best fits for different data sets
0.07 +- 0.005 (HIT April 2019)
0.09 +- 0.005 (HIT November 2018)
0.08 +- 0.005 (MedAustron March 2018)
Solution? Fit ranges with all Birks values and give difference as uncertainty
But not really clear why there is this difference. Probably small differences in the shape of the PDL curves (calibration?)
Unfortunately didn’t measure two of the same energies in Apr19 and Nov18 that we could compare

---
Birks’ constant
HIT Apr19
MedAustron
HIT Nov18