## Slide 1: Fitting Heavy Ion PDLs with Quenched Bortfeld Model
Saad Shaikh

## Slide 2: Requirements for “Successful” Fitting
He and C have different quenched model constants (α, β, γ, ε, p), found by Laurent from GEANT4 simulation.
  I need to learn how to do this for myself…
Fit range restricted to avoid fragmentation tail after Bragg peak.
Normally give initial fit parameter (R0, σ, Φ0, Birks) values by fitting Bortfeld model to FLUKA ddds and extract values.
Without any reference FLUKA sims for He and C, initial fit parameters are estimated…

## Slide 3: Estimating Initial Values of Fit Parameters
R0 estimated by linear approx. of position of 80% of largest value in measured data.
σ estimated by Gaussian fit to Bragg peak… but this gave values too large due to poor spatial resolution of detector in Bragg peak region (especially for sharp peaks of ions). Decided to fix σ to specific value:
  1.0 for He
  0.1 for C
Φ0 rough guess based on values from FLUKA proton sim, just need to get this in the right ballpark.
Birks constant could just be set at initial guess used for protons in our detector, 0.070

## Slide 4
Proton beam, (for comparison)

## Slide 5
Helium beam, σ = 1.0

## Slide 6
Carbon beam, σ = 0.1

## Slide 7: Discussion
Bortfeld model doesn’t perform too badly… but we shouldn’t have to fix σ and ignore the fragment tail in order to get a fit.
Carbon demonstrates more quenching than helium and both demonstrate more quenching than protons, as expected.
Carbon fits perform better than helium? We would expect this to be the other way round as helium has less fragmentation…
  The deviation shown in residual plot of helium looks like that of protons, but accentuated (as expected).
  Perhaps the constants of the model for carbon extracted from GEANT4 need to be checked? Good reason for me to learn how it’s done.
Birks constant should increase with heavier ions(?), but the value for carbon is even less than that of protons (which is around 0.07).
Not much that can be done without reference curves to compare with… will continue research into how to incorporate fragmentation into our model.