## Slide 1: NEMO-3 and SuperNEMO A search for zero neutrino double beta decay
Robert L. Flack
University College London
On behalf of the NEMO-3/SuperNEMO collaborations
NOW 2010

## Slide 2
2
Allowed by the standard model
Irreducible background in the search for 0
Input into NME calculations
0
Not allowed by the standard model
Neutrino must be Majorana
New physics mechanisms may contribute e.g Majaron
arXiv: 1005.1241
Why event reconstruction is useful
Powerful background rejection tool
If we observe 0 then studying the 2e, 1e energy + angular distributions will give information about the production mechanism.
Majaron

## Slide 3
3 m
4 m
B (25 G)
20 sectors
Source: 10 kg of  isotopes
cylindrical, S = 20 m2, d ~ 60 mg/cm2
Tracking detector:
drift wire chamber operating
in Geiger mode (6180 cells)
Gas: He + 4% ethyl alcohol + 1% Ar + 0.1% H2O
Calorimeter:
1940 plastic scintillators
coupled to low radioactivity PMTs
Magnetic field: 25 Gauss
Gamma shield: Pure Iron (d = 18 cm)
Neutron shield: 30 cm water (ext. wall)
40 cm wood (top and bottom)
(since march 2004: water + boron)
Particle ID: e-, e+, g and a
Fréjus Underground Laboratory : 4800 m.w.e.
The NEMO-3 detector
Neutrino Ettore Majorana Observatory

## Slide 4: Event reconstruction
Observables of the final state
  Trajectories of the 2 electrons
  Energies of the 2 electrons
  Time of flight
  Curvature of the tracks in a B-field (+ or -).
Source foils
Scintillator
+ PMT
Longitudinal view
Transverse view
Vertex of the e-e- emission
Vertex of the e-e- emission
NIM A606 (2009) 449-465.
Backgrounds are measured using event topology and timing to produce a background model for ββ

## Slide 5
T1/2(2nbb) = 7.11 ± 0.02 (stat) ± 0.54 (syst)  1018 years, S/B = 40
100Mo 2 updated result
Phys. Rev. Lett. 95 182302 (2005)
T1/2(2ν) = [7.17 ± 0.01(stat) ± 0.54(sys)] × 1018 yr ⇒ ~3.5 yr, Phase II (low Rn), S/B = 76
M2ν(100Mo) = 0.126 ± 0.006
This is an update of a previous published result using phase I data

## Slide 6
2νββ results for other isotopes (preliminary)
Many more results available. Excited states, 0ν for different mechanisms and isotopes
[9.6±0.1(stat)±1.0(sys)]×1019 yr
M2ν=0.049±0.004
[7.0+1.0-0.8(stat) +1.1-0.9(sys)]×1020 yr
M2ν=0.0173±0.0025
[2.35±0.14(stat)±0.16(sys)]×1019 yr
M2ν=0.049±0.002
96Zr
[9.20±0.25(stat)±0.63(sys)]×1018 yr
M2ν=0.030±0.002
[4.4+0.5-0.4(stat)±0.4(sys)]×1019 yr
M2ν=0.0238±0.0015
[2.88±0.04(stat)±0.16(sys)]×1019 yr
M2ν=0.0685±0.0025
130Te
116Cd
82Se

## Slide 7
0νββ for 100Mo(~7kg) and 82Se (~1kg)
[2.8-3.2] MeV: DATA = 18; MC = 16.4±1.4
T1/2(0ν) > 1.0×1024 yr at 90%CL
<mν> < (0.47 - 0.96) eV
V+A: T1/2(0ν) > 5.4×1023 yr at 90%CL λ < 1.4×10-6
Majoron: T1/2(0ν) > 2.1×1022 yr at 90%CL gee < 0.5×10-4 World’s best result!
[2.6-3.2] MeV: DATA = 14; MC = 10.9±1.3
T1/2(0ν) > 3.2×1023 yr at 90%CL
<mν> < (0.94 - 2.5) eV

## Slide 8
USA
MHC
INL
U Texas
Japan
U Saga
KEK
U Osaka
France
CEN Bordeaux
IReS Strasbourg
LAL ORSAY
LPC Caen
LSCE Gif/Yvette
Marseille
UK
UCL
U Manchester
Imperial College
Warwick
Finland
U Jyvaskula
Russia
JINR Dubna
ITEP Mosow
Kurchatov Institute
Czech Republic
Charles U Praha
IEAP Praha
Marocco
Fes U
Slovakia
(U. Bratislava)
~ 100 physicists, 10 countries, 27 Institutions
Spain
U Valencia
U Saragossa
U Barcelona
SuperNEMO Collaboration

## Slide 9
7 kg
100+ kg
isotope mass M
18 %
~ 30 %
isotope
100Mo
82Se or other
NEMO-3
SuperNEMO
internal contaminations
208Tl and 214Bi in the ββ foil
Rn in the tracker
208Tl: ~ 100 μBq/kg
214Bi: < 300 μBq/kg
Rn: 5 mBq/m3
208Tl ≤ 2 μBq/kg
if 82Se: 214Bi ≤ 10 μBq/kg
Rn ≤ 0.15 mBq/m3
T1/2(ββ0ν) > 2 x 1024 y
<mν> < 0.3 – 0.9 eV
T1/2(ββ0ν) > 1 x 1026 y
<mν> < 0.04 - 0.11 eV
energy resolution (FWHM)
8% @ 3MeV
4% @ 3 MeV
efficiency ε
Objectives of the 4 year R&D programme

## Slide 10
Calorimeter R&D to improve energy and time resolution
Scintillator
Material
Shape
Size
Coating
FWHM = 4% @ Qββ = 3 MeV
Required resolution demonstrated
with 28cm Hex block (≥10cm thick)
directly coupled to 8” PMT
Each module will have 550 PMTs + scintillator blocks
PMT
QE
Uniformity
Collection efficiency
Radiopurity

## Slide 11: Tracker R&D
To optimise the length, diameter, material for the wire, readout and gas mixture
Constructed several prototype single cells of differing lengths and diameters.
Then progressed to a 9-cell to look at the configuration of the fields and cross-talk.
From this work a 90-cell prototype was constructed.
Transverse 0.7mm, longitudinal 1cm
Overall cell efficiency of >98%
Cosmic muon used for testing of reconstruction algorithm

## Slide 12
Wiring robot
For the full 20 modules in excess of 0.5M wires will need to be strung.
A wiring robot is being developed at the Mullard Space Science Laboratory.
The wiring will be carried out in a clean-room environment with as little human intervention as possible.
Protoype robot being developed at MSSL
90-cell opened up

## Slide 13
Production of the ββ Source Foil
Dedicated BiPo detector to measure low radio-purity levels
Preferred candidate for the source is 82Se (others being investigated).
Enrichment of 100 kg by centrifugation is possible.
The density on the foil is 40-50 mg/cm2.
Radio-purity: 208Tl < 2 μBq/kg, 214Bi < 10 μBq/kg
Chemical and physical purification methods

## Slide 14: LSM Extension
Safety tunnel construction start - Sep 2009
Safety tunnel, end of civil construction - End 2011
Detailed study of LSM extension (ULISSE) - 2010
Deadline for final decision/money commitment - May 2011
Excavation of new Lab completed - mid-2012
Outfitting completed, Lab ready to host experiments - 2013
Schedule
Minimal scenario: 45,000m3 (100m long), 12M€ excavation + 3M€ outfitting
2d ULISSE workshop in October. 11 LOIs received.

## Slide 15
5yrs with 100kg 82Se:
T1/2(ββ0ν) > 1 x 1026 y
<mν> < 0.05 - 0.1 eV
Using a GEANT-4 based model of the detector combined with NEMO-3 experience.
82Se
Detector sensitivity

## Slide 16
Source 2.7m
Submodule
tracker
Submodule
calorimeter
Submodule
Source and calibration
6 m
4 m
2 m (assembled, ~0.5m between source and calorimeter)
A SuperNEMO module
Closed
Open
20 modules having a Planar design:
Each module will have 5kg of enriched isotope
Making a total of 100 kg.

## Slide 17
1st SuperNEMO module - Demonstrator
0.3 expected bkg events in 2.8 - 3.2 MeV with 7kg of 82Se in 2 yr
Sensitivity by 2015: 6.5∙1024 yr (90% CL)
Equivalent to 3∙1025 yr for 76Ge (using phase space ratio only)
or ~4 expected “golden events” if KK claim is correct
Demonstrate that mass production is possible.
Study the backgrounds with an emphasise on radon emanation.
Make a competitive physics measurement

## Slide 18: SuperNEMO schedule highlights
NEMO-3 decommissioning - early 2011
Demonstrator construction - 2010-2012
Demonstrator physics run start-up - 2013
Full detector construction start-up - 2014
Target sensitivity (~0.05 eV) - 2019
KK claim to be verified with Demonstrator by 2015

## Slide 19: BACKUP

## Slide 20
NEMO 3 under construction at the LSM

## Slide 21
100Mo 6.914 kg
Qbb = 3034 keV
82Se 0.932 kg
Qbb = 2995 keV
116Cd 405 g
Qbb = 2805 keV
96Zr 9.4 g
Qbb = 3350 keV
150Nd 37.0 g
Qbb = 3367 keV
Cu 621 g
48Ca 7.0 g
Qbb = 4272 keV
natTe 491 g
130Te 454 g
Qbb = 2529 keV
bb2n measurement
External bkg
measurement
bb0n search
(Enriched isotopes produced by
centrifugation in Russia)
bb decay isotopes in NEMO-3 detector

## Slide 22
232Th (208Tl) and 238U (214Bi) contamination inside the ββ source foil
Radon (214Bi) inside the tracking detector
- deposits on the wire near the ββ foil
- deposits on the surface of the ββ foil
220Rn
218Po++
External γ (if the γ is not detected in the scintillators)
Origin: natural radioactivity of the detector or neutrons
Main bkg for ββ2ν but negligeable for ββ0ν
(100Mo and 82Se Qββ~ 3 MeV > Eγ(208Tl) ~ 2.6 MeV )
NEMO-3 Backgrounds for ββ
Each bkg is measured using the NEMO-3 data

## Slide 23
214Bi → 214Po (164 μs) → 210Pb
β−
α
214Bi on the wires
β−
delayed
α
Example: Radon inside the tracking detector
214Bi → 214Po → 210Pb
β
α
(164 μs)
214Bi on the surface of the source foil
T1/2=162.9 μs
Delay time of the α track (μs)
Pure sample of 214Bi − 214Po events
Phase 1: Feb. 2003 → Sept. 2004
Radon Contamination
Phase 2: Dec. 2004 → Today
A (Radon) ≈ 5 mBq/m3
Monitoring of the Radon bkg every day

## Slide 24
1 ton of charcoal @ –50oC, 9 bars
air flux = 150 m3/h
Input: A(222Rn) 15 Bq/m3
Output: A(222Rn) < 15 mBq/m3 !!!
reduction factor of 1000
Phase I : February 2003 – September 2004 (radon background in data)
~ 1 0nbb-like event/y/kg with 2.8 < E1+E2 < 3.2 MeV
Radon trapping facility
Inside the NEMO 3 tent: factor of 100 – 300
Inside NEMO 3: almost factor of 10 A(222Rn)  6 mBq/m3
Phase II : since October 2004 (radon level reduced by a factor of 6)
Radon trapping facility
(First developed for SuperKamiokande)

## Slide 26
Physics Studies
Full chain of GEANT-4 based software + detector effects
+ NEMO3 experience
5 yr with 100kg of 82Se:
T1/2 > 1026 yr, <mν> < 50-100 meV at 90%CL
with target detector parameters
82Se
Much more than 1 result!
Other mechanisms: V+A, Majoron, etc
Disentangling <mν> and V+A:
arXiv: 1005.1241
ββ0ν(and 2ν) to excited states

## Slide 27: Open-minded search for any 0νββ mechanism
θ - angle between e1 and e2
can be due to
,V+A, Majoron, SUSY, H-- or a combination of them
E1 - single e- energy, keV
Topology can be used to disentangle
underlying physics mechanism
Topology detection is a more sensitive method for
phenomena with continuous spectra, e.g.
2νββ, 0νββB (Majoron)
Majoron
〈mν〉
V+A