## Slide 1
Particle-Driven Plasma Wakefield Acceleration
James Holloway
University College London, London, UK
PhD Supervisors:
Professor Matthew wing
University College London, London, UK
Professor Peter Norreys
Central Laser Facility, Rutherford Appleton Laboratory, UK

## Slide 2: Current RF Accelerators
Accelerate particles within a metal cavity.
Accelerated using an alternating electric field.
Electric fields greater than ~100 MVm-1 will ionize the metal itself.
--> To reach higher particle energies one has to increase the length over which the particles are being accelerated.
The Livingston plot shows the switch on time of hadron and lepton
colliders at the energy frontier as a function of achieved energy.
Plasmas can support higher electric fields. A plasma of number density
ne = 1014 cm−3 can support electric fields of E = 1 GVm−1.
Notes: Big tunnels are expensive!
To reach peta eV regime would need an accelerate half as long as earth’s circumference!

## Slide 3: What is PWA?
Short proton beam
+
+
+
+
+
+
-
-
-
Neutral plasma
Proton Beam
Novel particle acceleration technique
Can also drive wakefields with
Electrons
Photons
Positrons
Muons (in principle)
Notes: Mention electrons are ‘blown out’ instead of sucked in my e- and photons. Wakefield is the same, but shifted by PI in phase

## Slide 4
See movie file, Movie_p4.pptx
Notes: Mention electrons are ‘blown out’ instead of sucked in my e- and photons. Wakefield is the same, but shifted by PI in phase

## Slide 5: The Plasma
Lightning
Inertial confinement fusion
Interstellar plasma
Plasma frequency
 | Interstellar plasma | Lightning | Inertial confinement fusion
ne (m-3) | 105 | 1024 | 1032
Emax (Vm-1) | 30 | 1011 | 1015
λp (m) | 3 x 102 | 3 x 10-5 | 3 x 10-9
Maximum supportable E field
Notes: Plasma density dictates the maximum electric field the plasma can support, and the length of the driver required to effectively drive a wakefield.
We simulate at ~ 10^20. -> lambda p = 3mm. Still short!
We simulate cold hydrogen plasma. Sufficient unless you drive high amplitude wakefields.
Ions start to move -> distrupts the wakefield!
Need to then use heavier ions, ie ceasium, argon etc.

## Slide 6
The Diamond Light Source
The Diamond light source, RAL.
The Diamond light source at RAL uses a 3 GeV electron beam to generate soft x-rays.
The beam is generated by a 90 KeV electron gun that injects them into the Linac, which brings
it to ~ 100 MeV. The booster then brings it to 3 GeV then finally the storage ring maintains the
energy whilst cooling the beam.
Beam length: σz = 2.6 cm -> too long to effectively drive a wakefield. (λp ~ mm).
A proof of principle experiment has been proposed
to micro bunch the beam using the self modulation
instability, with the future intent to use the treated
beam to:
Create a higher energy electron beam
Create a poor mans FEL using betatron
oscillations within the wake
Imprint the modulated density profile of the
Diamond beam onto a proton beam, seeding
the modulation onto the proton beam

## Slide 7: The Self-Modulation Instability
Long proton beam
Neutral plasma
Affects long drive beams.
+
+
+
+
+
+
-
-
-
Microbunches are spaced λp apart.
Charge density increased.
Micro bunch lengths are much
closer to the ideal driver length of:
λp /π
These properties then allow the modulated beam to drive a wakefield much more effectively.
+
+
+
+
+
+
-
-
-
Neutral plasma
Self-modulated driver beam
Notes: Transverse vs longitudinal modulation. Say Ex and Ey are comparible in magnitude, however, lorentz factor in forward direction makes longitudinal modulation a minor contribution.
Talk about focusing / defocusing pohases.

## Slide 8
Linac
Pictures by Michael Bloom, Imperial College.
90 KeV

## Slide 9
Booster
Pictures by Michael Bloom, Imperial College.
158m circumference

## Slide 10
The Diamond Experiment
Serveral slides of tour of Diamond!
Transfer
Line
Pictures by Michael Bloom, Imperial College.

## Slide 11
The Diamond Experiment
Serveral slides of tour of Diamond!
Storage Ring
Pictures by Michael Bloom, Imperial College.

## Slide 12
Simulations
Simulations so far:
Untreated Diamond beam from the booster
-> Drove a weak wakefield
Cooled beam (2.7 nm rad) from the storage ring
-> Drove a weak wakefield
Radially compressed beam – using quadrupole
-> Filamentation instability dominated
Cut beam
-> Drove a weak wakefield. E = 70 KVm-1
Seeded beam – using an ideal driver
Diamond Booster Parameters
Energy 3 GeV
Geometric emittance 140 nm rad
Rms relative energy spread 0.0007
Rms bunch length 2.6 cm
Charge up to 2 nC
Typical simulation parameters:
4320 x 320 grid. ~ 107 particles
127 cores over 4 days
ne = 1.11 x 1020 m-3
-> λp = 3.17mm

## Slide 13
The untreated Diamond beam:
Before:
After:
Rear view Side View
Simulation of the untreated Diamond beam.
Energy 3 GeV
Geometric emittance 140 nm rad
Rms relative energy spread 0.0007
Rms bunch length 2.6 cm
Charge up to 2 nC
Set:
--> σr = 1.58 mm
T = 1 x 108 K
No Micro bunching
Mild filimentation
Simulations

## Slide 14
Radially compressed Diamond beam. -> Higher charge density drives a stronger wakefield.
Simulation of the untreated Diamond beam.
Set:
--> σr = 0.158 mm
T = 1 x 1010 K
Filamentation destroys the beam.
Cannot compress smaller than
σr ~ 1.58 mm.
Simulations

## Slide 15
Initial wakefield driven by ultra short pulse. σr = σz = 0.144 mm. Charge = 102 nC. nbpeak = 5 x 1018 m-3
Diamond beam then propagates in that wakefield and becomes micro bunched.
Simulation of the Diamond beam propagating with a wakefield.
Simulations
E = 3 MVm-1

## Slide 16
Upcoming Simulations
Next set of simulations:
Small parameter scan over intensities of seeding laser pulse
Modulated Diamond bunch into second plasma stage
Modulated Diamond bunch co-propagating with non-modulated proton bunch.
Inject witness electron beam and use motion to calculate synchrotron radiation
If our simulations demonstrate modulation of the Diamond beam is feasible and we
secure the beam time and the funding then this experiment should go ahead in 2012.
Laser Parameters:
λ = 1 μm.
Spot size = ~50 μm Diameter
I = 1013 – 1015 Wcm-2
Pulse length ~ 500 fs

## Slide 17
Thanks for listening