## Slide 1: Benchmarking proton CT reconstruction algorithms
Matthieu Hentz
CDT in Data Intensive Science at UCL
Working on proton CT in the HEP group
Supervised by Simon Jolly, Simon Arridge, Jamie McClelland

## Slide 2: Proton Beam Therapy
Amount of energy per unit path length transferred to an absorber is described by Bethe-Bloch equation (Schulte et al., 2005):
Notes: Mainly electronic interactions

## Slide 3: Proton Beam Therapy
increases rapidly as approaches zero
Leads to a sharp peak as particle comes to a stop -> Bragg peak
Amount of energy per unit path length transferred to an absorber is described by Bethe-Bloch equation (Schulte et al., 2005):

## Slide 4: Proton Beam Therapy
Amount of energy per unit path length transferred to an absorber is described by Bethe-Bloch:
increases as decreases
Leads to a sharp peak as particle comes to a stop

## Slide 5: Proton Beam Therapy
Control range of beam inside patient by choosing initial energy
More normal tissue is spared behind the target thanks to sharp drop in fluence
Dose in front of target (and overall) is lower compared to x-rays

## Slide 6: Proton Beam Therapy
Control range of beam inside patient by choosing initial energy
More normal tissue is spared behind the target thanks to sharp drop in fluence
Dose in front of target (and overall) is lower compared to x-rays
Under- or overshoot can be very damaging
Need to carefully plan treatment to minimise risk to critical structures
Matthieu Hentz

## Slide 7: Treatment Planning
Need a map of relative stopping power (RSP) for range and dose calculations
Can specify critical structures and beam directions and optimise plan iteratively
Requires 3D distribution of the attenuation coefficient (x-rays) or RSP (protons) in patient
Acquired using CT
Plan for proton beam therapy
Plan for x-ray therapy

## Slide 8: X-ray Computerised Tomography
The integral of a function along the straight line parametrised by its perpendicular distance from the origin, and its orientation with respect to the -axis, , is given by its Radon transform
-function ensures only values of along the path appear in the integral

## Slide 9: X-ray Computerised Tomography
The integral of a function along the straight line parametrised by its perpendicular distance from the origin, and its orientation with respect to the -axis, , is given by its Radon transform
-function ensures only values of along the path appear in the integral

## Slide 10: X-ray Computerised Tomography
The Radon transform is useful because the intensity of a photon beam exiting an absorber is given by
so
Can calculate the right-hand side by measuring
Applying the inverse Radon transform yields a map of the attenuation coefficient

## Slide 11: Analytical Reconstructions
Popular due to their computational simplicity
Example: Fourier transform reconstruction
  The 1D Fourier transform of the Radon transform of a function is equal to a central slice of the 2D Fourier transform of that same function:
  Can reconstruct by applying inverse 2D Fourier transform

## Slide 12: Issues with X-ray CT
RSP map currently obtained by converting from Hounsfield units using calibration curve
Increases range uncertainty
Treatment volume needs to be made larger to account for uncertainty

## Slide 13: Issues with X-ray CT
RSP map currently obtained by converting from Hounsfield units using calibration curve
Increases range uncertainty
Treatment volume needs to be made larger to account for uncertainty
X-ray CT suffers from streaking artefacts between high-Z regions in material: gold teeth, hip replacements, etc.
Fix: use protons to probe RSP directly and get rid of artefacts for free

## Slide 14: Proton CT
Fundamental constants
Particle properties
Material properties
Amount of energy per unit path length transferred to an absorber is described by Bethe-Bloch equation (Schulte et al., 2005):

## Slide 15: Proton CT
Fundamental constants
Particle properties
Material properties
Amount of energy per unit path length transferred to an absorber is described by Bethe-Bloch equation (Schulte et al., 2005):
electron number density,

## Slide 16: Proton CT
Dividing by the stopping power in water, :

## Slide 17: Proton CT
We can therefore express stopping power as
Integrating gives
This looks a lot like the Radon transform, except that integral is over curves rather than straight lines
: relative electron density
: stopping power in water
: mean ionisation potential of water
: trajectory of proton

## Slide 18
Many nuclear small-angle scattering events when traversing matter: multiple Coulomb scattering (MCS)
Lateral and angular displacement are normally distributed via central limit theorem
Leads to blurring in the reconstructed image
Can reduce blurring by estimating most-likely path (MLP) but this requires knowledge of entry and exit positions and directions
Challenges in Proton CT

## Slide 19
Single tracking has shown best (theoretical) performance
Two trackers on either side required to record entry and exit positions and directions to be used in calculation of MLP estimate
Calorimeter measures residual energy to determine WEPL traversed by the proton
(Krah et al., 2018)
Typical Proton CT Setup

## Slide 20
Most studies investigate algorithms in ideal conditions
Different algorithms have different properties
  Convergence and computational speed
  Severity of artefacts
  Propagation of noise
Want to know how algorithms perform with different imaging parameters
Parameters include the number of protons used, the beam energy, energy spread, detector resolution
Reconstructions performed on simulated data
Benchmarking
Notes: Acquisition time

## Slide 21
Profile across line segment inserts
Edge response across line segment inserts
Modulation transfer function (MTF)
RSP accuracy
(Rit et al., 2013)
Metrics

## Slide 22
Different phantoms can be used to assess different image properties
Resolution can be measured using CTP528 module of the Catphan phantom
Use phantom with aluminium inserts in spiral pattern to assess radial dependence of resolution
Phantoms
Catphan CTP528 module
Spiral

## Slide 23
Geant4 v10.4.2
Multithreading provides roughly 7x speedup
Fan beam of 200 MeV protons
288e6 protons in total
Phantom is rotated whilst protons are recorded on detector before and after
720 projections, one every 0.5°
Preliminary Simulations
Notes: Acquisition time

## Slide 24
Geant4 v10.4.2
Multithreading provides roughly 7x speedup
Fan beam of 200 MeV protons
288e6 protons in total
Phantom is rotated whilst protons are recorded on detector before and after
720 projections, one every 0.5°
Preliminary Simulations
Notes: Acquisition time

## Slide 25
Spiral
Catphan CTP528
Used analytical algorithm (Rit et al., 2013)
This algorithm is popular due to its speed
Both reconstructions took less than 25 seconds to compute
Preprocessing takes about 6 minutes on cluster with 20 nodes
Preliminary Reconstructions
Notes: Acquisition time

## Slide 26
Preliminary Reconstructions
Compared spiral reconstruction to the “perfect” phantom
RSP of aluminium inserts is about 2.13
Absolute difference between reconstruction and phantom is shown
Notes: Acquisition time

## Slide 27
Future Work
Simulate detector effects
Get access to and learn how to use other reconstruction algorithms
Compare algorithms
Notes: Acquisition time

## Slide 28
Questions?
Notes: Acquisition time