## Slide 1: Running simulation with Open Topas
10/11/2025
Guided by Joe Bateman
(for pristine Bragg Curve)

## Slide 2: Open Topas Documentation
https://opentopas.readthedocs.io/en/latest/parameters/material.html
Some important ones are under materials, scoring, particle sources

## Slide 3: Needed file
Runxx.txt
  Acts like the initial configuration of the world (defining geometrics)
      s:Ge/phantom/Material = "G4_WATER" - indicate watertank standardized to water anyway.
      s:Ge/phantom/Parent = "World"
        defaulted to box of 10mx10mx10m
        beam comes at +5m side
      s:Ge/phantom/Type = "TsBox" - the box the shape for the tank standardized
      d:Ge/phantom/TransX = 0 cm
      d:Ge/phantom/TransY = 0. cm
      d:Ge/phantom/TransZ = 4.8 m
        indicating where the translational of
      d:Ge/phantom/HLX = 10 cm
      d:Ge/phantom/HLY = 10 cm
      d:Ge/phantom/HLZ = 10 cm
        The size of detector in half length.. it shows 20cmx20cmx20cm
      i:Ge/phantom/ZBins = 200
      i:Ge/phantom/YBins = 200
      i:Ge/phantom/XBins = 200
        Bins tells the precision 200 bins for 20cm.. 1mm precision
      s:Ge/phantom/Color = "yellow"

## Slide 4: Needed file
pbx.txt (check scoring documentation)
  change the beam energy to your needed one
  change beam particle to genericion(6,12) for protonif needed if needed. check documentation under particle sources.
  number of histories run (number of particle you are using): defaulted to 1M particles
  cutoff for pbt always, gaussian and ellipse. then you have to define cutoffx and y, otherwise it will go infinitely like gaussian curve.

## Slide 5: Needed File
topas_submit_xx.sh
  Shell script to run and submit jobs
edit the topas_submit_xx.sh
  for i in (1..x) where x is the number of pbx.txt
  change the cd to the right directory

## Slide 6: CSV to generate pbx.txt
energy spread define the stddev of the bragcurve peak. Clinically consistent, heidelberg 0.8MeV. Topas energy spread equal to 0.8Mev/Energy*100
sigmax sigma y, is the beam size x and y gaussian stddev
Column filled with
Pb (integer 1 to x), sigmax, sigmay, energy, energy spread, posx, posy
Then run the topas_generator.py to generate the pbx.txt

## Slide 7: Steps to run simulation
Having the runxx.txt
having the pbx.txt
copy the topas_submit_xx.sh and rename it
ssh to 188: ssh febian@pc188.hep.ucl.ac.uk
edit the topas_submit_xx.sh
run it in terminal ./topas_submit_xx.sh
to run only 1,
  run qsub -q medium pb245mevjob.sh
Once running, it will give nasty csv of 200x200x200 bin results
run the script to get it to nice CSV data topas_bragpeak2.py

## Slide 8: Running Simulation With Geant4
18/11/2025
Guided by Joe Bateman
(for Scintillating QuARC)

## Slide 9: Steps
Copy folder from Joe directory
ssh febian@plus1.hep.ucl.ac.uk
mkdir geant4
cp -r /home/jbateman/simulations/Geant4/QuADProBe/quarc_g4_10_6_batch/ /home/febian/geant4
cd quarc_g4_10_6/
cd macros/
nano inter.mac

## Slide 10: Env setup
cp /home/jbateman/simulations/pbt_cvmfs_setup_g4_10_6.sh /home/febian/geant4
chmod +x pbt_cvmfs_setup_g4_10_6.sh
source /unix/pbt/software/scripts/pbt.sh -g 9 -G 10.6
  (needed for the first time sourcing the environment)
./pbt_cvmfs_setup_g4_10_6.sh
[quarc_g4_10_6]$ nano ProtonSimulation.cc
  Ensure that the G4String defaultmacro pointing to the right inter.mac directory.

## Slide 11: Inter.mac file
Adjustable parameter:
  /control/alias nProtons 1000000
  /control/alias beamEnergy 90 #MeV, shoot-through energy at MedAustron
  /control/alias beamEnergySigma 1.14 #MeV
  /control/alias beamSize 3.84 #mm sigma (FWHM/2.355)
  /control/alias stepMax 500 #mu
  /control/alias rangeCut 1000 #mu
  /control/alias beamAngle 0 # 0.0349 #0.0875 #is in units of tangents
  #these geometry parameters are NOT updated in PTDetectorConstruction, but still need to be correct for output of data
  /control/alias nLayer 200 # this and below number don't set the parameters in PTDetectorConstruction
  /control/alias zLayer 3 #3 #mm

## Slide 12: Notes
Updating the
  /control/alias nLayer 200 # this and below number don't set the parameters in PTDetectorConstruction
  /control/alias zLayer 3 #3 #mm
Required further update in PTDetectorConstruction.cc file under src folder
  Line 69, scintZPlate (3)*CLHEP
  Line 71, nScint = (200)
    Match the number within the bracket with the one in inter.mac

## Slide 13: Running the simulation
source /unix/pbt/software/scripts/pbt.sh -g 9 -G 10.6
  (needed for the first time sourcing the environment)
cd to build folder and run
  cmake -DCMAKE_CXX_STANDARD=17 -DCMAKE_BUILD_TYPE=Release -DGEANT4_USE_QT=ON -DGeant4_DIR=/cvmfs/geant4.cern.ch/geant4/10.6/x86_64-centos7-gcc9-optdeb-MT /home/febian/geant4/quarc_g4_10_6
  Make
  To quick test its running
    Edit the inter.mac nProtons to100
    ./ProtonSimulation

## Slide 14: Output
Under the output folder
EdepAccurate_150MeV_200x3_500mustep_100p_refl.out
  energy deposition within the quarch at 500µm steps
LeftSideScorer_150MeV_200x3_500mustep_100p_refl.out
RightSideScorer_150MeV_200x3_500mustep_100p_refl.out
  photodiode areas but need really big nproton
NPhoton_150MeV_200x3_500mustep_100p_refl.out
  light generated at each sheet (This is one we prolly need to use, the results is quenched)
NPhotonLeft_150MeV_200x3_500mustep_100p_refl.out
NPhotonRight_150MeV_200x3_500mustep_100p_refl.out
  The photons that reaches the left or right side of the scintillator sheet

## Slide 15: Submit the job to the cluster
cd build
edit run_g4sim_1.sh
  Make sure they are right directory
    # Set up the environment
    source /home/febian/geant4/pbt_cvmfs_setup_g4_10_6.sh
    # Change to the simulation directory
    cd /home/febian/geant4/quarc_g4_10_6/build
qsub -q medium run_g4sim_1.sh