## Slide 1: QuADProBe Development Path
Simon Jolly
PBT Group Meeting
22/07/2025

## Slide 2: Current Status
QuARC
  Successful beam tests with 2-sided readout using 8 boards, USB104 and Raspberry Pi 5.
  DAQ now entirely web-based.
  12 new DDC boards recently delivered from Oxford.
QuADProBe:
  Bari SciFi setup with basic NI-based DAQ tested.
  Heidelberg have developed SciFi profile monitor with FPGA readout for HIT.
  NPL Transmission Calorimeter in development.

## Slide 3: QuARC Requirements
ALL beam tests show how vital matched sheets are! New sheets needed from Nuvia to be machined at UCL (Barnett).
DAQ limited by number of USB104 channels: more channels also needed for QuADProBe.
Shock absorption system needs lowering to align scintillator modules with central case axis; new version needed for lid.
Update to single 100W USB-C/DC power supply with internal distribution board (Hastings).
Gantry mounting hardware needed (IBA, Prague+Barnett).
Small changes to case (Barnett):
  Wheels mounts.
  Alignment plates.
Is Apache+D3 optimal for live web display? Python web server possible but static? To be investigated by MSci student (Saeed).
Move to 4 boards, photodiode arrays and 2.5 mm pitch…?

## Slide 4: QuADProBe Requirements
Need scintillating fibre arrays: Bari/Heidelberg (Radogna/Bateman).
Current DAQ too limited: cannot adapt Heidelberg system in its entirety.
  Imperial Kria-based front end.
  Imperial to design Kria carrier (Rose).
Hamamatsu photodiode arrays best current option but analogue/digital versions not yet set:
  Analogue better dynamic range?
  Digital requires less front end electronics.
  Front-end interface board still needed (Hastings).
Arrays will need holder and mechanical structure (Barnett).
NPL Transmission Calorimeter to be integrated later: spare DAQ channels helpful!

## Slide 5: Nozzle Mount

## Slide 6: Heidelberg Beam Monitor (Leverington)

## Slide 7: Heidelberg Photodiode Arrays

## Slide 8: Hamamatsu Photodiode Boards

## Slide 9: Heidelberg ADC Board

## Slide 10
Z-mod to "usb-c" adapter
USB3
$350
£75
FPC
FPC

## Slide 11
Custom Breakout Board
$325
"usb-c"
"usb-c"
"usb-c"
GbE phy+RJ45
SATA M.2?
PCIe M.2?
USB?
Single 12V supply in
← ×2.5
← ×5
← ×0.6
← ×5000
c.f. Rpi5 + USB401

## Slide 12
10cm
10cm
First guesstimate of a board design from ripping up a Serenity s1.3 design
Sata M.2
Kria
uSD card
GbE
"usb-c"
Power

## Slide 13
x1?
x1?
x1
x4
x1
x1
x4
x4
x4
x4
4xUSB-C for data 1 for control
x4
x1

## Slide 14: Kria Carrier Board Layout

## Slide 15: Kria SciFi Readout
Option 1
Option 2

## Slide 16: Kria QuARC Readout Option 1

## Slide 17: Kria QuARC Readout Option 2