## Slide 1: Testing/Debugging Matt Code
14/01/2026

## Slide 2: Background
To understand the new changes
To test the new changes works and function as how it was
To be able to adapt it to the KRIA board

## Slide 3: Issue 1: Different version Vivado
Matt is using Vivado 2024.2, I am using 2022.1 (widely used version for Kria KV260)
Upon opening xpr and all the source from Matt repo, it only open in read-mode. Requires save project as (done it) - too many errors
  IP configuration/file can’t be found (even after re-created, does not get detected by the workspace)
  Old components IP FIFO2kx8 and FIFO8kx8 is no longer used, removed the file from the file project, but still required to be in the hieararchy.
  no val for da elab attr error (different version renderer issue)
  ….
  Hence give up fixing it as fixing 1 error leads to another follow ups error.

## Slide 4: Attempt 1: recreate the project
The solution is to recreate the project under vivado 2022.1
  The syntax remains the same, so just copy and paste the content from Matt sources while maintaining the hierarchical files.
Issue 1: error in using work.pkg_types.all
  Pkg_types.all is a custom library made for typing variables. It’s not listed in hierarchical but existed in sources libraries. Add design sources needed.
Further error encountered.
  integer_vector has not been declared
    Commented out all this integer_vector
  Process(all) construct only supported in VHDL 1076-2008.
  Noticed all the files in the library is render with VHDL 2019
    Enter in TCL Console:
set_property FILE_TYPE {VHDL 2008} [get_files *.vhd]

## Slide 5: Continue
Synthesis success Implementation failed.
  Design place error. IO placement is infeasible. Number of unplaced terminals (268) is greater than number of available sites (200). The following Groups of I/O terminals have not sufficient capacity: IO Group: 0 with : SioStd: LVCMOS18 VCCO = 1.8 Termination: 0 TermDir: Out RangeId: 1 Drv: 12 has only 200 sites available on device, but needs 268 sites.
  Apparently, the board/FPGA parts selected from the list is wrong. Xc7z010iclg225 is used which refer to zynq 7 zybo board not artix-7. Artix-7 option is not there due to the space constraint when installing vivado and enabling Kria board to be installed instead.

## Slide 6: Fixing: add the board manually
There is list of boards provided by digilent: https://github.com/Digilent/vivado-boards/tree/master?tab=readme-ov-file
Old boards is for vivado 2014.x and below, any newer vivado version uses the new boards directory.
New/board_files copy it to C:/Xilinx/Vivado/2022.1/data/boards/
  Does not get detected
Different approach: Open new project, select boards, refresh catalog
  Install the boards
  The boards disappeared despite installed successfully.
Add installation – via main page – help – add design tools or device
  Don’t know why Xilinx required disk space is unreasonably large.
  Install success, Implementation success.

## Slide 7: Program the device
Generate bitstream + bin file
Generate Memory config file
  USB104 memory config: s25fl128xxxxx0-spix1_x2_x4
  From tools – generate memory config file – format mcs – interface SPIx1
  Right click on the hardware – s25fl…. - program config memory device
Program the device. Close the hardware manager.
Setup DAQ module 1, test using GUI run on Kria apache.
Works as expected.

## Slide 8: New changes in FW
Using XPM Async FIFO library instead of IP FIFO
XPM (Xilinx Parameterised Macros) async FIFO is like a built in library
  Only for Async FIFO designed for clock domain crossing feature. (IP FIFO is configurable)
  Stable across different Vivado version whereas IP FIFO required upgrade and regeneration of IP.
  Stable and predictable, very lean implementation, resource optimized.
  Requires manual HDL wiring and understanding whereas IP FIFO is highly configurable via GUI.
  Only has basic FIFO flags and functionality, unable to interface AXI stream (might need to get back to IP FIFO for KRIA as SoC communication uses AXI)

## Slide 9: Summary
Removed the extremely long shift-registers from ddc232.vhd
  Shift registers uses in IP FIFO reserves LUT as buffer storage and FF for synchronisers. Free up when uses XPM Async FIFO.
Currently, code built with 8 module capability. Note that old code will get smaller if built with fewer modules, the new code will not.
Old version (3704f8): LUT: 15.4% FF: 5.5% BRAM 1.85% New version (3aa5df): LUT: 0.8% FF: 0.5% BRAM 1.85%

## Slide 10: Notes
CDC = Clock Domain Crossing
  A clock domain is a part of a design that runs on a specific clock. A CDC occurs when a signal passes from one clock domain to another with a different clock (different frequency, phase, or completely unrelated).
Why CDC is a problem?
  If you sample a signal generated by Clock A using Clock B, the signal can change close to Clock B’s edge and cause:
    Metastability (flip-flop output is temporarily undefined)
    Data corruption
    Intermittent bugs that are hard to reproduce

## Slide 11
Aspect | XPM Async FIFO | FIFO Generator IP (IP FIFO)
Integration method | HDL instantiation (library macro) | Generated IP core via Vivado IP Catalog
Clock domain crossing | Designed specifically for safe CDC (async FIFO) | Supports async and sync FIFOs (configurable)
Portability | High portability across Xilinx devices and tool versions | Tied to Vivado IP flow and project
Tool dependency | Minimal (no IP regeneration needed) | Strong dependency on Vivado IP management
Customization | Parameterized but limited to common FIFO features | Highly configurable (depth, widths, flags, ECC, etc.)
Ease of use | Requires manual HDL wiring and understanding | Easier for beginners via GUI
Simulation setup | Simple; no IP simulation models needed | Requires generated simulation files
Synthesis predictability | Very predictable, officially recommended by Xilinx | Predictable, but regeneration may change internals
Resource optimization | Efficient, lean implementation | Can be slightly heavier due to feature richness
Advanced features | Basic FIFO flags (full, empty, almost full/empty) | Advanced options (ECC, FWFT, programmable thresholds, AXI interfaces)
Version control friendliness | Excellent (pure HDL, no generated files) | Weaker (generated files and metadata)
Long-term maintenance | Stable across Vivado versions | May require IP upgrade between Vivado versions
Debug visibility | Limited built-in debug features | Better integration with Vivado debug tools
Xilinx recommendation (recent) | Strongly recommended for CDC FIFOs | Still supported but less favored for simple FIFOs
XPM vs IP FIFO

## Slide 12: AXI Stream
AXI-Stream is not just data + valid/ready. It has strict protocol rules and optional sideband signals:
Core rules
  TVALID must remain asserted until TREADY is high
  TDATA must remain stable while TVALID && !TREADY
  Transfer happens only when TVALID && TREADY
  Backpressure must be handled cleanly
Optional but common signals
  TLAST (packet boundaries)
  TKEEP / TSTRB
  TID, TDEST, TUSER
A compliant AXI-Stream FIFO must:
  Keep all sideband signals aligned
  Preserve packet boundaries
  Maintain ordering
  Obey timing guarantees even under backpressure
XPM FIFO Flow
Not AXI-Stream compliant
Not aware of AXI timing semantics
Not verified against AXI spec
No FWFT guarantees in AXI terms
write_en, din → FIFO → dout, read_en

## Slide 13: Intro to AXI
AXI stands for Advanced Extensible Interface and is part of the AMBA (Advanced Microcontroller Bus Architecture) standard developed by ARM for SoC designs. It was introduced in AMBA revision 3.0 to support high-performance, high-frequency interconnects.
An AXI transaction comprises:
  Address & control phase
  Data transfers (in bursts)
  Response phase (especially for writes)
Each transfer beat within a burst must complete all beats specified.
AXI is designed to be: Modular, High-performance, Low-latency Flexible
AXI pairs well with interconnect fabrics that connect multiple masters and slaves.
It supports complex SoC topologies where many components (DMA, processors, accelerators) must communicate efficiently.

## Slide 14: Key Features of AXI
Multiple Dedicated Channels
  AXI uses five separate channels between a master and a slave:
    Read Address
    Read Data
    Write Address
    Write Data
    Write Response These channels allow address/control and data to be transferred independently, increasing performance.
Independent Handshakes
  Every channel uses VALID/READY handshake signals to control data transfer. Data moves only when both signals are asserted, which helps with flow control and rate matching.
Burst Transfers
  AXI supports burst transactions—multiple data beats in a single transfer.
  Burst behavior (length, size, type) is programmable, improving efficiency for large transfers.
Out-of-Order Completion
  Transactions carry IDs that allow them to complete out of order relative to each other while maintaining ordering for each ID. This improves throughput.
Additional Signals
  AXI includes optional sideband signals such as cache control, protection, and lock signals for atomic or exclusive access, and optimization hints.