## Slide 1: PS PL data stream
28/01/2025

## Slide 2: PL – PS BRAM Connectivity
Block RAM (BRAM) is on-chip memory integrated inside FPGA fabric.
Pre-built memory blocks Distributed throughout the FPGA (PL), Directly connected to logic, DSPs, and processors
Accessible by: PL logic and PS (via AXI interconnect)
Much faster than external memory (DDR), Low latency, Predictable timing, however: Limited capacity
Used for data buffering, storage, and control

## Slide 3: BRAM Port Configuration
Single-port RAM
  One port, Can read OR write in a clock cycle (not both independently)
Simple dual-port RAM
  Two ports, One is read-only, One is write-only,
  Separate read and write clocks (optional)
  Write and read can happen in the same cycle
  Addresses are independent
True dual-port RAM
  Two fully independent ports, Each port can read OR write, Same time, same or different addresses

## Slide 4: Design Block
Open design block required following components:
  ZYNQ Ultrascale+ MPSoC
  AXI Interconnect
  Rst_ps_9, processor system reset
  AXI BRAM Control
  Define external input using CTRL+T
Run the auto connect feature
Run validation check, save generate block design
Right click on the design source, create VHDL Wrapper

## Slide 5: Add design source, top
Top.vhd to implement a 32-bit counter register using block memory generator.
Connect the Design_1_wrapper to the block memory generator.
  If rising_edge(clk), if rst = 1, addr, din, we (write enable) set to 0
  Else: if addr != FULL, addr = addr+1, din = din +1, we= 1, else we = 0.
Generate bitstream, export hardware, include bitstream
Launch Vitis IDE

## Slide 6: Vitis IDE application project
Open new application project
  Cortexa_a53
  Select project helloworld (needs UART peripheral on the hardware. This needs to be added when designing block ZYNQ MPSoC IP.
Open the source helloworld.c
  Defined address u32 *address = Null;
  Address = (u32 *) XPAR_AXI_BRAM_CTRL_0_S_AXI_BASEADDR;
  Iterate through using for loop. Print address
Right click on the side bar, build project. Debug program.
  Expected 0x00000001, 2, and so on.
  Obtained: error while launching program from vitis IDE. Memory write error at 0x0 cortexa-53#0 editr not ready

## Slide 7: Next steps
Investigating the issue, is it a design issue? or vitis issue? Project build in vitis on top of the design is fine. The FW design is fine as well but not quite working
Once the above is done, it could be implemented with the Sci-fi array.
Check DMA (Direct memory access) allows writing directly to DDR on PS side. Particularly useful as it allows larger size of data to be written.
  4GB build in DDR
  300 18Kb BRAM blocks around 5Mb