## Slide 1: BOC1 Run Thru:
Agenda
14h30 Start CB Local Meeting
16h00 Break for Tea
16h30 Start Telephone Conference
18h00 Conclusions
18h30 Finish

## Slide 2: BOC1 Run Thru:
Provides the interface between ROD and Detector Modules
Provides the interface between ROD and ROBs
Receives Clock from TIM via backplane, provides copy for ROD.
Also provides ancillary timing functions
What BOC Does
Outline

## Slide 3: BOC1 Run Thru:
ROD <-> Module interface:
  Clock and Command streams to modules
    clock-control encoding and timing trims
    electrical to fibre-optic conversion
  Data streams from modules
    fibre-optic to electrical conversion
    data sync and timing functions
ROD <-> ROB interface:
  Electrical to Opto with error detection and correction plus flow control
Outline

## Slide 4: BOC1 Run Thru:
BOC0 was the proof-of-principle board
  Full scale (48 command, 96 data streams)
  Available components (opto & ASICs)
    BPM4 & Current Mirrors & Quad VCSELs
  Test bench for some circuits
  Full functionality
    (inc. Some Pixel 80MHz streams)
BOC0

## Slide 5: BOC1 Run Thru: .
Provides VME access to BOC via Set-Up Bus - @ front of crate in place of ROD
allows SLOG to drive all 48 command streams (fanned out from 12)
selects 12 of the 96 data streams for Mustard
Provides specialised test facilities:
  SNAPshot of the 12 selected streams
  SCOPE MODE
  generation of 80MHz Pixel test data
BOC-RIG

## Slide 6: BOC1 Run Thru: .
Does all v1 does
provides 12 un-encoded command streams in optical form to give 12 SLOG-derived opto signals for BOC data stream testing.
The 80MHz Pixel data mode should work for 6 of these streams
Board Manufactured, but not fully tested
BOC-RIGs key to BOC1 testing
BOC-RIG v2

## Slide 7: BOC0 Test Results: .
Set-Up Bus operations work fine:
  read and write to BOC registers generally OK
      Manufacturer # top bit sometimes wrong: hole in ROD or BOC logic code .. Fix very unlikely to need schematic change
  write to BPM4 registers OK (BPM4 read-back known not to work)
  write to laser current DACs OK (serial path)
  write to data threshold DACs OK (serial path)
  write to data delay chips OK (I2C path)
  write to clock delay (fine and coarse) OK
  write to clock control ccts OK … but will change
Set-Up Bus

## Slide 8: BOC0 Test Results: .
Wrong pin-out for PIN array means streams reach ROD in wrong order
  not worth fixing on BOC0 ..
  simply fixed on BOC1
The eye-pattern looks very good:
  threshold scans not completely clean: probably due to laser deficiences
  delay scans show timing jitter on looped-back data of well less than 1ns
The Streams implemented in CPLDs OK
  De-Muxing from 80MS/s to 40MS/s is good
Data Streams

## Slide 9: BOC0 Testing:
Check the S-Link:
  S-Link components still not complete (awaiting the ODIN Link Source Card)
Controlling modules ?
  Slow command data from modules?
    .. Eg. Front-end registers
  Data from Modules ? .. real and calibration
  System set-up operations:
    designing and refining procedures
    are the provisions good enough?
Yet To Do:

## Slide 10: BOC1 Run Thru:
BOC1 is the pre-production prototype:
  using production compatible components
  should move seamlessly into production
BOC1

## Slide 11: BOC1 :
A (remarkably small) number of PCB fixes
Reduce PCB depth to 220mm (was 240mm)
Add Power Monitor and Power-up Reset
Clock Circuit changes:
  fail-safe provision (PLL?)
  implement a couple of BOC0 patched mod’s
  double range of fine clock delay to 5ns
  reduce short-term jitter
  guarantee mark-space
Move to New Opto and ASICs: see next slide
Improve laser interlock provision
Differences

## Slide 12: BOC1 : .
BPM12 is major rework of BPM4:
    12 streams rather than 4
    drives common cathode lasers
    many other improvements
New Plug-In Opto Modules by Academica Sinica of Taiwan:
    4 x OpTX .. BPM12, VCSEL12 & 2x MDACs (Laser Current)
    8 x OpRX .. DRX12, PIN12 & 2x MDACs (Threshold)
    size: 21x30mm
    each OpTX replaces 3x BPM4s, 3x Mitel VCSEL4s, 12 current mirrors & 1.5 MDACs
    each OpTX replaces 1x DRX12, 1x Mitel PIN12 & 1.5 MDACs
MultiDAC mapping more difficult:
    changes to control circuitry
New Opto .. Details

## Slide 13: BOC1 Run Thru: .
New Opto
Academica Sinica OpRX Prototype

## Slide 14: BOC1 Run Thru: .
Interlocks
Block Diag. Unchanged!
With Optional
80MS/s - 2x40MS/s
De-Muxing

## Slide 15: BOC1 Run Thru. .
VCSEL arrays
BPMs
Laser Current - DACs+Amps
Current Mirrors
PIN arrays
DRX amp/discrim
Pixel Compatible
Streams
Data Delay Chips
T/Hold DACs
Data Registers
Clock Circuits
BOC0 Layout
S-Link Source Card

## Slide 16: BOC1 Run Thru. .
OpTX Plug-Ins
Data Stream CPLDs (80MS/s - 40MS/s De-Mux capable)
Data Delay Chips
LVDS Receivers
Clock Circuits
BOC1 Layout
S-Link Source Card
OpRX Plug-Ins
Command Stream CMOS Buffers
Data to ROD
Clock From TIM
Set-Up Bus from ROD
Events from ROD
Commands from ROD

## Slide 17: BOC1 Run Thru: .
BOC0 v BOC1 Layout
Data RX Section
Clock
Section
Ctrl
CPLD
S-Link
Section
Clock and Command
Section
BOC0

## Slide 18: BOC1 Run Thru: .
PIXEL Working
PIXEL BOC .. Layers B and 1

## Slide 19: BOC1 Run Thru: .
PIXEL Working
PIXEL BOC .. Layers 2 and Disk

## Slide 20: BOC1 Run Thru: .
PIXEL Working
PIXEL BOC .. 80MS/s - 2x 40MS/s De-Muxing
I/P
(80MS/s)
Data
Delay
0-24ns

## Slide 21: BOC1 Run Thru: .
PIXEL Working
PIXEL BOC .. 80MS/s - 2x 40MS/s De-Muxing

## Slide 22: BOC1 Run Thru: .
PIXEL Working
PIXEL BOC .. 80MS/s - 2x 40MS/s De-Muxing

## Slide 23: BOC1 Run Thru: .
Schematics
The Full set of BOC1 Schematics can be found in BOC1_Drgs.pdf
Sheet 1:
  J2 & J3 Connections
  Power Monitors
  VPIN regulator for PIN Bias Voltage
Sheet 2:
  Clock Generation Circuitry and Fan-Out
Sheet 3:
  Control CPLD
  Fallback Crystal Oscillator
  Interlock Circuits
  Indicator LEDs
Sheet 4:
  Set-Up Bus Buffering
  CMOS Buffers for BPM Control Signals
  S-Link Wiring
  Shadow RAM for Readback of Serial Data
Sheets 5-6: Clock and Command
  OpTX Module Connections and Buffering
Sheets 7-10: Data Receiver Streams
  OpRX Modules
  LVDS Data Receivers
  PHOS4 Data Delay chips
  Data Stream CPLDs
  LVDS Clock Receivers
Sheet 11:
  MultiDAC Control
  CPLD In-System Programming Connectors
Sheet 12:
  Data Stream Buffers for ROD Interface

## Slide 24: BOC1 Run Thru: .
Layout

## Slide 25: BOC1 Run Thru: .
Layout

## Slide 26: BOC1 Run Thru: .
Clock Detail

## Slide 27: BOC1 Run Thru: .
Clock & Command

## Slide 28: BOC1 Run Thru: .
Data RX Section