## Slide 1: ATLAS Pre-Production ROD Status SCT Version
April 30, 2002

## Slide 2: Design Overview: SCT version (Simplified Block Diagram)
SLINK
I/O
32MB
SDRAM
DSP0
TMS320C6701
32MB
SDRAM
DSP1
TMS320C6701
32MB
SDRAM
DSP2
TMS320C6701
32MB
SDRAM
DSP3
TMS320C6701
Formatter 0
Links 0 - 11
XCV400E-6FG676
Formatter 1
Formatter 2
Formatter 3
Formatter 4
Formatter 5
Formatter 6
Formatter 7
Event
Fragment
Builder
XCV400E-6FG676
Router
XCV300E-6FG456
Input
Debug FIFO Bank A
---
Data Path Mux
Input
Debug FIFO Bank B
---
Data Path Mux
Input
Debug FIFO Bank A
---
Data Path Mux
Input
Debug FIFO Bank B
---
Data Path Mux
Master DSP
TI - TMS320C6201
16MB SDRAM
VME Interface
Cypress CY7C960A
CY7C964
Chip set
FPGA Program Reset Manager
ROD Controller
Xilinx
XCV600E-6FG676
Links 12 - 23
Links 24 - 35
Links 36 - 47
Links 48 - 59
Links 60 - 71
Links 72 - 83
Links 84 - 95
XCV200E-6FG456
12MB FLASH

## Slide 3: ROD Test Status : Slave DSPs
Remaining Basic Functionality Tests:
Slave DSP:
  The Slave DSP boot and data transfer OK.
  SDRAM memory tests OK on Slave DSP 0.
  SDRAM errors on Slave DSPs 1, 2 and 3 on all boards.
    The exact problem has not yet been identified. We need to determine if the errors occur on reads or writes, and if they are due to the ROD Controller FPGA which is used to transfer data to and from the Slaves, or by noise on the output enable signal used on the Router to transfer the Event Data to the DSP, or by some other hardware mechanism.

## Slide 4: ROD Development Status : Hardware Changes
VME Host to ROD Communication:
  Converted the VME to DSP HPI access to D32. This access was D16 previous to the modification.
Program Reset Controller FPGA:
  Added code to allow D32 access from the VME host to the Master DSP Host Port Interface.
  Modified FLASH R/W algorithm to minimize VME cycles required. DMA is not allowed on the ROD Flash memories.
Master DSP (TMS320C6201):
  Changed 6201 core voltage to match TI’s revised specification. All core type devices on ROD are now at 1.85V. (The FPGAs and Master DSP require 1.8V, and the Slave DSPs require 1.9V. Because we have 1 core supply, we must split the difference.)

## Slide 5: ROD Development Status : Hardware Changes (2)
ROD Controller FPGA:
  Re-organized the memory map to simplify ROD Configuration.
  Added a test mode to allow the Input Memory FIFOs and the Internal TIM FIFO to retransmit 4K of Event Data up to 65535 times.
  Modified VHDL to allow 32 bit access from the Master DSP to all of the Slave DSP HPI ports. (The DSP HPI is a 16 bit bus). This change allowed DMA from the VME host to the Slave DSP internal and external memories.
Event Fragment Builder FPGA:
  Removed Formatter Masking algorithm from the VHDL. This was originally required because of a bug in the Formatter VHDL which was fixed before the last review.
Router FPGA:
  Fixed Frame Transfer Interrupt bug in VHDL
Slave DSP (TMS320C6701):
  Increased SDRAM size from 16MB to 32MB.

## Slide 6: ROD Status : Things to do
Fix the Slave DSP SDRAM Memory Bugs.
Modify VHDL to incorporate all proposed ROD Modes.
  ROD Controller FPGA:
    Add required logic to allow stand alone calibration and advanced testing of modules. The additions will be in the form of counters, registers, and other miscellaneous circuits required by the final algorithm. This should be about 2 to 4 weeks of writing, building, and debugging.
    Add ECRID Counter to the Event ID Data Encoder Block when required. (Some changes will also need to be made to the EFB VHDL.)
    Add logic required to trap Pixel register data into the InMem FIFOs.
  Router FPGA:
    Add required logic to modify Router trapping algorithm to meet the requirements defined in the ROD Hardware and Software Upgrade document. This should be about 1 week of writing, building, and debugging.

## Slide 7: ROD Status : Things to do (2)
Miscellaneous:
  Investigate increasing the size of the Internal TIM FIFO from 4K to 8K to increase the number of events that can be played into the Formatters from the Input Memories.
  Finalize implementation of ROD Controller Modes.
  Fine tune, clean up, and modify the VHDL code for all of the ROD FPGA devices as requirements defined by the ATLAS Community change.
    e.g. implementation of an ECRID Count in the L1ID word of the Event Header; modifications to the “Start of Event” word…
  Continue writing the ROD Operating Manual to describe how the ROD functions.
  Continue development of the Test Procedure Document that will be used to perform initial tests and as a trouble-shooting manual.
  Continue work on all changes required to accommodate the PIXEL front ends.