## Slide 1: SCT and Pixel Off Detector Electronics Status June 25, 2001
Cambridge : Back Of Crate (BOC) card (optical interface) and SCT DAQ, Andy Parker, John Hill and Maurice Goodrick
Wisconsin : Read Out Driver (ROD)
Khang Dao, Damon Fasching, Douglas Fergusson, Richard Jared, John Joseph, Mark Nagel, Sriram Sivasubramaniyan (Ohio State) and Lukas Tomasek and Jan Valenta (Institute of Physics AV CR, Prague)
University College London: Timing Interface Module (TIM),
Jon Butterworth, John Lane, Martin Postranecky and Matthew Warren
Oxford Crate Backplane
Roy Wastie
Iowa State Pixel DAQ,
Roy McKay,Tom Meyer and Eli Rosenberg
Richard Jared

## Slide 2: SCT and Pixel Off Detector Electronics Status June 25, 2001
Material Covered:
Overview of Off Detector electronics
Back Of Crates Card (BOC)
Read Out Driver (ROD)
Timing Interface Module (TIM)
DAQ
Cambridge System Test
Schedule

## Slide 3: SCT and Pixel Off Detector Electronics Status June 25, 2001
Components of the Off Detector Electronics
Back Of Crate (BOC) card (optical interface), Cambridge
Read Out Driver (ROD), Wisconsin
Timing Interface Module (TIM), University College London
Crate Backplane, Oxford
SCT DAQ, Cambridge
Pixel DAQ, Iowa State
Overview

## Slide 4: SCT and Pixel Off Detector Electronics Status June 25, 2001
Overview

## Slide 5: SCT and Pixel Off Detector Electronics Status June 25, 2001
TIM (Timing Interface Module)
Receives clock and trigger information from the TTC
Transmits clock and trigger information to the ROD
Receives busy information from the ROD
Masks and passes on busy to the L1 Trigger
Operates stand alone under control of the RCC
RCC (ROD Crate controller)
Reads configuration data from the ATLAS data base
Configures the TIM, ROD and BOC
Controls the operation of the crate
Monitors the crate during running
Provides readout, control and configuration in stand alone mode
Overview

## Slide 6: SCT and Pixel Off Detector Electronics Status June 25, 2001
BOC (Back of Crate Card) (ROD optical fiber interface)
Receives optical module data and formats data for the ROD input
Receives module control data from ROD and formats data for the optical fibers
Provides individual fiber delays
Houses the Slink interface
ROD (Read Out Driver)
Formats input data
Provides latency FIFOs
Corrects header and trailer errors
Corrects header and trailer
Counts errors
Provides for calibration of modules
Traps and monitors event data
Formats data for Slink input
Overview

## Slide 7: SCT and Pixel Off Detector Electronics Status June 25, 2001
    Current Status:
    BOC prototype, (BOC-0 ):
    BOC-0 was the proof-of-principle board
    Full scale (48 command, 96 data streams)
    Full functionality (inc. Some Pixel 80MHz streams)
    BPM4 rather than BPM12
    Quad VCSELs to match BPM4
    Current-mirrors match BPM4 I-sink outputs to common
    cathode VCSEL arrays
    Testing showed:
    Communications with ROD works fine
    TX: Clock and Command stream OK
    RX: Data Stream OK
    Eye pattern good
    Timing measurement procedure OK
    De-muxing of PIXELS 80 MS/s data demonstrated
Back Of Crates Card

## Slide 8: SCT and Pixel Off Detector Electronics Status June 25, 2001
    Current Status:
    BOC1 is the pre-production prototype:
    Using production compatible components
    Should move seamlessly into production
    Changes from BOC0:
    A (remarkably small) number of PCB fixes
    Reduce PCB depth to 220 mm (was 240 mm)
    Add Power Monitor and Power-up Reset
    Clock Circuit Changes
    Pll with fail-safe provisions ??????????
    Increase range of fine clock delay to 10ns in 10ns steps
    should give reduced short-term jitter and guaranteed mark-
    space
    Move to New Optical and ASICs: see next slide
Back Of Crates Card

## Slide 9: SCT and Pixel Off Detector Electronics Status June 25, 2001
    Current Status:
    New Opto and ASICs
    BPM12 is major rework of BPM4
    12 streams rather than 4
    Drives common cathode lasers
    Many other improvements
    New Opto Plug-In Modules by Academica Sinica of Taiwan:
    4 x OpTX per BOC … BPM12, VCSEL12 & 2 x MDAC (Laser
    Current)
    8 x OpRX per BOC … DRX!@, PIN12 & 2 x MDACs (Threshold)
    Allows better testing & far easier rework
    Size:21 x 30mm
Back Of Crates Card

## Slide 10: SCT and Pixel Off Detector Electronics Status June 25, 2001
Back Of Crates Card
Data RX Section
Clock
Section
Ctrl
CPLD
S-Link
Section
Clock and Command
Section
BOC0

## Slide 11: SCT and Pixel Off Detector Electronics Status June 25, 2001
BOC1 Status:
PCB manufactured (11 ea.) - Done
Parts delivered (for 11 BOCs) - end of Feb. 02
Assembly of first 2 BOCs - early Mar.
Receipt of 5 TX & 5 RX Opto Plug-Ins - mid Feb.
Receipt of 5 TX & 5 RX Opto Plug-Ins - mid Mar.
Limited by lack of ASICs
Serious testing - thru to end April
ASIC supplies (BPM and DRX) - expected May
Up to 11 BOCs for SCT & Pixel community - this Summer
partial population until new ASICs available for Opto Plug-Ins
Final PCB changes - June/July
Back Of Crates Card

## Slide 12: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)

## Slide 13: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
Evnt
Frg
Bldr
Fifo0
Evnt
Frg
Bldr
Fifo1
Router
Event
Fragment
Builder
DSP3
Fifo/Buffer
DSP2
Fifo/Buffer
DSP1
Fifo/Buffer
DSP0
Fifo/Buffer
DSP3
Module
DSP2
Module
DSP1
Module
DSP0
Module
Link 0DATA 1b
Link 11DATA 1b
Link 12DATA 1b
Link 23DATA 1b
Link 24DATA 1b
Link 35DATA 1b
Link 36DATA 1b
Link 47DATA 1b
Link 48DATA 1b
Link 59DATA 1b
Link 60DATA 1b
Link 71DATA 1b
Fifo 40b
DATA
Fifo 40
DATA
Fifo 40b
DATA
Fifo 40b
DATA
Fifo 40b
DATA
Fifo 40b
DATA
EvntFrgBldr
DATA 46b
EvntFrgBldr
DATA 46b
Event 46b
Header/Trailer
Events 46b
Events 32b
Trapped 32b
DATA
Trapped 32b
DATA
Trapped 32b
DATA
Trapped 32b
DATA
SLINK 1b
TIM EventDATA 16b
TIM TriggerDATA 8b
from TIM
Processed 16b
Trapped
DATA
Processed 16b
Trapped
DATA
Processed 16b
Trapped
DATA
Processed 16b
Trapped
DATA
SLINK
Event Fifo
32bx4W
SLINK
Link 72DATA 1b
Link 83DATA 1b
Link 84DATA 1b
Link 951DATA 1b
Fifo 40b
DATA
Fifo 40b
DATA
Formatter
Fifo0
Formatter
Fifo1
Formatter
Fifo2
Formatter
Fifo3
Formatter
Fifo4
Formatter
Fifo5
Formatter
Fifo6
Formatter
Fifo7
DataValid 1b
VME Bus
BOC
To Formatter
ROD Controller

## Slide 14: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
data formatter FPGAs
real time data path
master DSP
& memory
controller
FPGA
boot
FPGA
program FLASH
power supplies
slave DSPs & memories
router
FPGAs
event
builder
FPGA
debug &
derandomizing
memories
ROD bus
buffers

## Slide 15: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
Current Status
Production model RODs (4 ea.) have been fabricated.
Debugging is complete on two cards.
Cambridge has one production model ROD for system testing.
What hardware is working:
Data Flow
Through the Formatter, Event Fragment Builder and Router working
To the Slave DSP working
Initialization working
Communication to/from Slave DSP working
Running primitives in the Master/Slave DSP working
VME (A32,D16/D32) read/write to the ROD working
Read/write to debugging FIFOs
Read/ write to Formatter, Event fragment Builder, Router FPGAs
Read/write to the Controller FPGA
Read/write to the Back Of the Crate card
Controller FPGA is working.
Configuration of front end modules
Triggering of front end modules

## Slide 16: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
Current Status (continued)
Hardware upgrades need:
Lifted pin and VHDL to enable A32,D32 VME to Master DSP access
The Master DSP core voltage is changed (by TI) to 1.85V (wire jumper)
VHDL upgrades needed to enable DMA to Master and Slave DSPs
VHDL to enable trapping of module configuration return data (pixels)
VHDL to provide ROD based counters of BCOs, Triggers and registers
for event type related data for stand alone operation.
VHDL for recognition of fast command on the serial data streams from the
master DSP via the controller to the front end modules.
VHDL for changes to the hardware memory map update
VHDL changes as needed for problems or future new requirements.
.

## Slide 17: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
Current Status
Test Stand Software
The test stand software will be used for the early tests at Cambridge.
The test stand software is about 85% complete.
The remaining software is for the production test stand.
DSP Software:
DSP Software Status
The DSP primitive software will allow for Module/ROD/BOC configuration,
triggering of modules and read out of events to the crate processor.
DSP Software Upgrades Needed:
Making interrupts and BIOS work under Texas Instruments (TI) library 1.2
Upgrading to TI library 2.0
(note TI libraries 1.0, 1.2 and 2.0 are not compatible)
Improve the DSP processing of event data so it has event boundaries
not number of word boundaries
Activated histogram packages in the slave DSP
Make changes the user community needs as testing advances.

## Slide 18: SCT and Pixel Off Detector Electronics Status June 25, 2001
Read Out Driver (ROD)
Current Status
Projected schedule
Production Model RODs (4 ea.) have been fabricated
So far these 4 RODs will be part of the production RODs (100 ea.)
Parts and PC boards are in hand to fabricate 9 more RODS.
User evaluation from 2/02 till 5/02 is needed to have FDR of ROD.
Fabrication of 9 RODs will follow FDR.
PRR should be 8/02 for fabrication of RODs (total of 100)
Crates 8ea. will be purchased when CERN has the purchase order in place.
Concerns
User evaluation is needed for the ROD to proceed to production. There
needs to be much activity in the next 2 months to keep to the schedule.
The ROD is very complex. It is not known how easy it will be to debug
the cards. There is also concern with the number of defects in the
manufactured card. These effects are very manufacturer specific.
Significant effort is being made to find good manufacturers.

## Slide 19: SCT and Pixel Off Detector Electronics Status June 25, 2001
Timing Interface Module (TIM)

## Slide 20: SCT and Pixel Off Detector Electronics Status June 25, 2001
Timing Interface Module (TIM)
VME Buffers
EventID deMUX/
generate & FIFO
Sequencer
TTC to RODs
(PECL drivers)
VME Interface
Stand-alone Trig generate
EventID
Serializer
NIM/ECL Aux TTC I/O
RODBusy
TTCrx module

## Slide 21: SCT and Pixel Off Detector Electronics Status June 25, 2001
Timing Interface Module (TIM)
What have we done so far?
Four prototype TIMs made
Parts in hand for 6 more TIMs
TIM delivered to Cambridge in March 2001
Clock jitter at BOC input reduced to 100ps peak-to-peak
Corrections/modifications submitted for drawing at RAL.
What is working?
VME access to all registers & memory
Clock and sequencer (i.e. Programmable pattern generator)
TTC, front-panel, standalone and ROD Busy inputs
Event ID and backplane outputs.

## Slide 22: SCT and Pixel Off Detector Electronics Status June 25, 2001
Timing Interface Module (TIM)
Status update:
All CPLDs simulated
BCID offset is operational
TTCrx I2C interface is operational
Event ID logic is operational.
To do:
Debugging & Testing (ongoing)
Coding of VME interrupts (ongoing).
Concerns
Learning curve for FPGA implementation (just starting).
Plans and schedule
Six more TIMs (iteration of prototype) to be manufactured soon for Q2
Redesign/implement TIM using new parts ("final" system) for Q3 2002.

## Slide 23: SCT and Pixel Off Detector Electronics Status June 25, 2001
Crate Backplane
Accomplishments:
10 new Prototype backplanes have been fabricated.
7 backplanes have been shipped to various sites. (LBNL,UCL,CAM,NIKHEF)
Current Work:
Corrections of slots order 5-9, addition of CLK-OK line.
Concerns:
None

## Slide 24: SCT and Pixel Off Detector Electronics Status June 25, 2001
DAQ
Accomplishments:
Note: The pixel and SCT DAQ are expected to have much overlap of code.
Use cases have been studied to determine ROD DSP code partitioning
SCT and Pixel DAQ workshop was held last week.
Pixel DAQ has written several primitives for the slave DSP.
Pixel DAQ has written a memory test primitive.
SCT DAQ has generated the Cambridge system test plan
SCT DAQ has written code to communicate to the TIM.
Current Work:
Development of partitioning and functionality
Investigating the use of DAQ-1 for macro assembly sites.
Concerns:
The DAQ code is not written.
Manpower is limited.

## Slide 25: SCT and Pixel Off Detector Electronics Status June 25, 2001
Cambridge System Test
  Started 23 June - ROD prototype arrived at Cambridge
  Prototype testing
  Configuration of the ROD tested OK
  Configuration of the BOC tested OK
  Configuration of the TIM tested OK
  RCC was used to configure TIM and pattern generators.
  Event data was played from pattern generators t > electronic
  to optical converters > BOC > ROD > personal computer OK
  Module configuration was not tested and there were work a
  rounds for problem.

## Slide 26: SCT and Pixel Off Detector Electronics Status June 25, 2001
Cambridge System Test
  Production Model ROD Testing (arrived Cambridge Feb. 4th)
  Configuration of ROD tested OK
  RCC was used to configure TIM and pattern generators.
  Event data was played from pattern generators t > electronic
  to optical converters > BOC > ROD > personal computer OK
  The next test will be of front end module module configuration.

## Slide 27: SCT and Pixel Off Detector Electronics Status June 25, 2001
Production Schedule
The production ROD and BOCs will start when there is sufficient user evaluation to determine that they will perform the required functions.
Is is hoped that there will be sufficient user evaluation to have a FDR
at about 5-02
Small numbers of RODs (total of 13) and BOCs (total of 11) can then be produced as needed.
It is hoped that the continued user evaluation will be adequate to have the FDR about 8-02.
Production of the BOC, ROD and TIM can then proceed.