## Slide 1: SCT and Pixel Off Detector Electronics Status February 6, 2002
Timing Interface Module (TIM)
What have we done so far?
Four prototype TIMs made
Parts in hand for 6 more TIMs
TIM delivered to Cambridge in March 2001
Clock jitter at BOC input reduced to 100ps peak-to-peak
Corrections/modifications submitted for drawing at RAL.
What is working?
VME access to all registers & memory
Clock and sequencer (i.e. Programmable pattern generator)
TTC, front-panel, standalone and ROD Busy inputs
Event ID and backplane outputs.

## Slide 2: SCT and Pixel Off Detector Electronics Status February 6, 2002
Timing Interface Module (TIM)
Status update:
All CPLDs simulated
BCID offset is operational
TTCrx I2C interface is operational
Event ID logic is operational.
To do:
Debugging & Testing (ongoing)
Coding of VME interrupts (ongoing).
Concerns
Learning curve for FPGA implementation (just starting).
Plans and schedule
Six more TIMs (iteration of prototype) to be manufactured soon for Q2
Redesign/implement TIM using new parts ("final" system) for Q3 2002.