## Slide 1: SCT and Pixel Off Detector Electronics Status February 6, 2002
Timing Interface Module (TIM)
What have we done so far?
Ten prototype TIMs have been made
TIM delivered to Cambridge in March 2001 for system tests
TIM delivered to LBL in March 2002 (and NIKHEF MDT in Nov 2001)
TIMs ready for shipping to CERN and Oxford
Clock jitter at BOC input reduced to 100ps peak-to-peak.
What is working?
VME access to all registers & memory
Clock and sequencer (i.e. Programmable pattern generator)
TTC, front-panel, standalone and ROD Busy inputs
Event ID and backplane outputs.

## Slide 2: SCT and Pixel Off Detector Electronics Status February 6, 2002
Timing Interface Module (TIM)
Status:
All CPLDs simulated
BCID offset is operational
TTCrx I2C interface is operational
Event ID logic is operational.
To do:
Debugging & Testing (ongoing)
Coding of VME interrupts (ongoing).
Concerns
Learning curve for FPGA implementation (just started).
Plans and schedule
Redesign/implement TIM using new parts ("final" system) for Q4 2002.