## Slide 1
ROD RACK ELEVATION
OPTO-CABLES & RIBBONS SUPPORTS
MP-UCL, 07-09-2005
Open Slot Conduit Box (3) for TOP ROD Crate ( ONE or TWO boxes used depending on need for storage of Opto-Ribbons )
Opto-Ribbons for TOP ROD Crate
Opto-Cables for TOP ROD Crate
Opto-Cables for TOP ROD Crate
Opto-Ribbons for BOTTOM ROD Crate
Open Slot Conduit Box (3) for BOTTOM ROD Crate ( ONE or TWO boxes used depending on need for storage of Opto-Ribbons )

## Slide 2
ROD RACK 3-D VIEW
MP-UCL, 07-09-2005
OPTO-CABLES & RIBBONS SUPPORTS
Rack FRONT
Rack REAR
Opto-Cable Inner Support Brackets (4) ( on right or left side of rack )
Open Slot Conduit Box (3) ( ONE or TWO boxes used above each crate depending on need for storage of Opto-Ribbons)
Existing Opto-Cable Support Brackets ( on right or left side of rack )

## Slide 3
Rack FRONT
Rack REAR
ROD RACK FLOOR PLAN
R/A Bracket (1)
R/A Bracket (2)
Open Slot Conduit Box (3)
MP-UCL, 07-09-2005
OPTO-RIBBONS SUPPORT
Opto-Cable Inner Support Bracket (4)

## Slide 4
ROD Rack REAR LEFT SUPPORT
Open Slot Conduit Box (3)
R/A Bracket (1)
OPTO-RIBBONS SUPPORT
MP-UCL, 07-09-2005
Rack REAR
Rack INSIDE

## Slide 5
ROD Rack REAR LEFT SUPPORTS
Inner Opto-Cables Support Brackets (4)
Existing Opto-Cable Support Brackets
OPTO-CABLES BRACKETS
MP-UCL, 07-09-2005
Opto-Cables to Top ROD Crate
Opto-Cables to Bottom ROD Crate
Rack REAR
Rack INSIDE

## Slide 6
NOTES :
& (2) Steel right-angle brackets, 65 x 75 mm, 2 x M6 clearance holes - Total 32 required
Open Slot Conduit Box, Halogen-free Noryl HNG-type, 75 x 73 mm x 580 mm long, 5 mm wide slots at 12.5 mm pitch, ( eg. RS 296-0459 or ONECALL/CPC CBBR-6398 ) - Total 16 required
(4) Aluminium bracket, 30 x 3 mm x 325 mm long, 2 x M6 clearance holes at 308 mm centres spacing – Total 16 required
MP-UCL, 07-09-2005