## Slide 1: HEP Electronics
TIM Status Report
John Lane Martin Postranecky, Matthew Warren

## Slide 2: Status
TIM operates as a TTC destination or stand-alone.
TIM interfaces with a crate of ROD’s via a backplane.
10 working prototype TIM’s exist for assembly sites and development.
2 FPGA TIM’s (version 3A) being tested at UCL
  FPGA’s load test code from PROM’s
  Loan crate with P3 backplane arrived after delay
  Firmware largely written, but untested
Plan for further 18 TIM’s:
  - 8 SCT + 8 Pixels + Spares

## Slide 3: Moving to FPGA
10 CPLD’s reduced to 2 FPGA’s – Xilinx Spartan IIE.
32kB RAM and 64x128 FIFO moved into FPGA.
Most DIL’s replaced by SMD (excl. backplane interfaces.)
TIM2
TIM3A

## Slide 4: TIM3A
VME Buffers
ROD Backplane Mapping & PECL Drivers
FPGA1 XC2S200E (VME Interface)
NIM/ECL Signals I/O
TTCrm Module
J3 Backplane ROD Signals Output
TTC Fibre-optic Input
FPGA2 XC2S600E (TIM Functions)