## Slide 1: The DAVE Card Status
SCT has developed a new ATLAS trigger card
“The card that no-one knew they needed, but now do”
Introduction
Concept & Motivation
Functionality Overview
Production Status
ATLAS orders

## Slide 2: What is it?
6U VME Digital Atlas Vme Electronics (DAVE) card (acronym reflects a certain sense of humour by our engineers)
Design, production and firmware by UCL and Cambridge
  Maurice Goodrick, Rick Shaw (Cambridge)
  Matt Warren, Martin Postranecky (UCL)
Support and encouragement from ATLAS
  Strong support and ideas from Thilo Pauly, Carolina Gabaldone
  User case suggestions from Iskander Ibragimov, Bruce Barnett, Andrej Gorisek

## Slide 3: Concept & Motivation
Delay
Stretch
Pulse Generator
Trigger
Orbit (BCR)
L1A to LTP
NIM Crate – SCT USA15
VETO
We long wanted to eliminate use of a NIM crate in USA15 which provides our trigger for standalone physics runs
Contains veto logic (prevent BCR/L1A clash) which drifts
Need to go downstairs to adjust trigger rate
Non-realistic conditions
First thoughts were replace this simple logic in a VME card
Concept quickly grew to add more generic features
Significant enhancement to adopt ATLAS CTP functionality to exactly duplicate running conditions, whilst incorporating much generic functionality, has turned the card in a hugely powerful and flexible logic card, potentially useful to all ATLAS subsystems as well as for non-ATLAS use

## Slide 4
DAVE card: examples of CTP Functionality
ECRsel
VME
ECRin
period
ECR:
L
U
T
8
PS
MSK
Gate
Veto
OR
8
8
SHP
ExtTrigger
Trigger path:
8
4
1
1
L1Aout
TriggerOut
SD
CD
OR
BUSY
L1Ain
Veto:
1+1ms
ECRsel
ECRout
L1Aout
Veto
Internal
Playback
Fixed Freq
Internal Triggers:
RND
BG
2
2
4
6?
Internal
VCXO
BCout
BCin
BC/ORBIT:
DELAY25
QPLL?
internal
ORBin
ORBout

## Slide 5: Interesting use-cases
Trigger generator for LTP (via LEMO)
  no busy gating, feed-forward of deadtime to LTP
Standalone trigger generator without LTP
  busy gating
ECR generator
VETO generator
L1A (or other signal) sequence analyser
Sequence playback
  Eg capture and replay trigger sequences that causes susbsystem busy etc
BC/ORBIT source, fine-delay (dt=0.5-1ns) for timing scans
Generic delay line
Generic counter facility
  a few counters
  per-bunch counters?
Generic logic unit
  Programmable “NIM crate”

## Slide 6
3x LEDs
NIM
ECL
12x LEDs
3
3
3
3
3
SHIFT
REG.
2
CLKIN0
IN0
IN2
IN6
IN4
CLKIN1
CLKOUT0
OUT0
OUT2
OUT6
OUT4
CLKOUT1
SW
SW
SW
2
2
8
8
2
2
8
8
NIM
ECL
NIM
TTL
NIM
TTL
HEX SELECT
16-pin AUX. CONNECTOR
USB
J-TAG
X-TAL
80.15733MHz
MPX
PLL
:2
40/80MHz select
CLK Master DELAY
4x Slave DELAYS
4
4
4
CLKIN select
FPGA & PROM
2
8
4
8
16
6
2
16 ( incl. 4x 2V5 diff. LVDS )
SW
SERIAL NO.
MOD. RECORD
SW
SW
24
40-pin DIL BREAK-OUT HEADER
All POWER and GND rails
32
EXT. +5V IN
FUSES
+3V3 +2V5 +1V8 +1V2 -5V -2V
6x DC-DC
VME
J1
VME
J2
+5V
FUSE
Buffers
VME BASE ADDRESS
16
22
Data
4Mbx18
SRAM
Address
MP-UCL, 21 February 2011
20x LEMO-00
Buffers
All POWER Monitor
7
7
2x LEDs
ATLAS-SCT “DAVE-1” Programmable VME Module M.Goodrick, D.Robinson, R.Shaw @ University of Cambridge, Cavendish Lab M.Postranecky, M.Warren @ UCL
7
8
8
SHIFT
REG.
FPGA spec: Xilinx Spartan 3E 1600 (SC3S1600E)

## Slide 7
DAVE card – first prototype

## Slide 8: DAVE card Firmware Blocks
CTP-like Trigger Module
AND/OR matrix
Input
Enable
Sync
Delay
8
Busy Gen
Output
Enable
Map
Internal Sig Gen
Randomiser
Fixed Freq
BCR/BCID
ECR/ECRID
Sequencer
ECR Gen
BCR Gen
Fine Delay*
63x.5ns
Mask/ Gate
Dead-time
Not on FPGA
using CERN Delay25 chip
4
Sink RAM
VME/USB Interface
8
LEMO In
LEMO Out
Firmware mainly by Matt, USB by Maurice, testing by Rick
CTP blocks originally by Stefan Haas.
Higher level software to be provided by Thilo Pauly & Dave Robinson

## Slide 9: Production Schedule
3 prototypes already built
  Some minor design iterations pending
    Corrections made by wire-tack
Firmware already well underway and some basic functionality demonstrated
  USB functionality still pending
Next design iterations by ~March
First modules for testing by ~June

## Slide 10: ATLAS Orders
SCT (3)
TRT (2)
Pixels (2)
BCM (2)
ATLAS central trigger (3)
Strong interest by L1Calo and Lar
…others are likely

## Slide 11: Summary - Key Points
Communication by VME OR USB
  In vme crate or on desktop with power supply
Exact CTP functionality
  Random trigger, simple and complex deadtime, ECR, BCR etc to give exact same conditions in standalone as experienced in combined runs
Trigger sequence playback
  64M word SRAM gives us up to 52 seconds history of trigger playback for 75kHz L1 rate (eg on interrupt by system BUSY)
Powerful generic functionality
Available by ~summer – see them in TTC crates in USA15!