## Slide 1: Interesting use-cases
Trigger generator for LTP (via LEMO)
  no busy gating, feed-forward of deadtime to LTP
Standalone trigger generator without LTP
  busy gating
ECR generator
VETO generator
L1A (or other signal) sequence analyser
Sequence playback
BC/ORBIT source, fine-delay (dt=0.5-1ns) for timing scans
Generic delay line
Generic counter facility
  a few counters
  per-bunch counters?
BCM:
  generic logic unit
  typically TTL
  how many signals? 6?
  possibility to make logic at larger frequency?

## Slide 2
Block Diagram of DAVE card
ECRsel
VME
ECRin
period
ECR:
L
U
T
4
PS
MSK
Gate
Veto
OR
4
6?
4
SHP
ExtTrigger
Trigger path:
4
4
1
1
L1Aout
TriggerOut
SD
CD
OR
BUSY
L1Ain
Veto:
1+1ms
ECRsel
ECRout
L1Aout
Veto
Internal
Playback
Fixed Freq
Internal Triggers:
RND
BG
2
2
4
6?
Internal
VCXO
BCout
BCin
BC/ORBIT:
DELAY25
QPLL?
internal
ORBin
ORBout

## Slide 3: Comments
Delay-line
  stepsize 25ns
  range: at least 0..63 would be good, a full turn 0..3564 would be even better
Shaper
  edge sensitive or strobed by clock
  if strobed, need procedure to verify phase relationship
    e.g. with scope and BC-LEMO-output
  fine-delay with some fraction of 25ns
Clock:
  not sure if QPLL is really needed
  internal clock frequency should be near enough to the LHC frequency (40.0789)
  maybe useful to have two fine-delays, one for the clock that is used on the board and an independent one for the output LEMO (so one can change the phase between L1A and BC, needed for TTC crate fine-tuning)
Memory:
  it would be good if one could select any of the signals to be recorded in the memory (L1A, TriggerOut, ExtTrigger, VETO)
  maybe more than 1 signal?
  playback facility would be useful to be fed back as internal trigger
Veto:
  on/off switch for gate
  selection of which L1A to be used for preventive deadtime (simple+complex): either L1Aout or the LEMO input
BunchGroups (BG):
  Lists of 3564 BC, synchronised with ORBIT signal at programmable offset
Possibilities for running at higher clock speed?
  need more specific BCM requirements here
Counter facilities:
  would be useful to have 32bit counters at various stages, e.g. input, intermediate, output
  deadtime counters would be useful
  per-bunch monitoring could be very useful (3564 counters)
  could imagine turn counter for time normalization of counters

## Slide 4: Frontpanel + Compatibility
Input LEMO-00
BCin (NIM, ECL)
  LTP(NIM, ECL), TTCvi(NIM), TTCex(ECL), TIM(NIM)
ORBin (NIM, ECL)
  LTP(NIM,ECL), TTCvi(NIM)
4 or more external triggers (NIM, TTL)
  NIM logic, LTP(NIM,ECL?), TTCvi(NIM), TIM(NIM), BCM(TTL)
BUSYin (NIM, TTL)
  RODBusy(TTL,NIM), TIM(NIM), LTP(NIM,TTL)
L1Ain (NIM, TTL, ECL?)
  LTP(NIM,ECL?), TTCvi(NIM)
ECRin (NIM, TTL?)
  LTP(NIM)
Output LEMO-00
BCout (NIM,ECL)
  LTP(NIM), TIM(NIM), TTCvi(ECL), TTCex(ECL)
ORBout (NIM,ECL)
  LTP(NIM), TIM(NIM), TTCvi(ECL)
L1Aout (NIM,ECL)
  LTP(NIM), TTCvi(ECL,NIM), TIM(NIM)
4 trigger items (NIM,ECL)
  LTP(NIM), TTCvi(ECL,NIM), TIM(NIM)
ECRout (NIM)
  LTP(NIM), TTCvi(NIM), TIM(NIM)
VETOout (NIM,TTL)
  LTP(NIM,TTL), RODBusy(TTL), TIM(NIM)
Remark: need to carefully check electric compatibility for each board