## Slide 1
ATLAS-SCT : TIM-3C Status :
All 11x SCT TIM-3C ( Ser.nos.326-336) modules are at CERN
One used for DAQ development in SR1 ( Alan Barr )
Two used for the Barrel Test Crates in SR1 ( Peter Phillips )
Eight ( destined for USA15 SCT use ) stored in SR1
Additional two TIM-3C modules : one at UCL, one in Cambridge
One Pixel TIM-3C at CERN used in Pixel test crate
10x Pixel TIM-3Cs stored at UCL ( at their request )
All final TIMs production now finished : 24x TIM-3Cs plus 24xTIM-3Es for CSS and MDT
All SCT TIM-3Cs at CERN have the FFTV permanently enabled
Two TIM-3Bs ( functionally identical to TIM-3C ) : 1x Cam., 1x LBL
Spare components for estimated 10-years usage stored at UCL

## Slide 2
SCT DAQ Software Development :
DAQ and Test software is being actively worked on at CERN, currently using the SCT End-Cap test crate and TIM-3C ( UCL : Alan Barr , CAMBRIDGE : John Hill )
Very good progress had been made and number of changes to TIM-3C firmware identified, made and tested to facilitate the DAQ and Tests software development
Currently, all SCT and Pixel TIM-3Cs have the same “(final-1)” firmware installed. It is proposed to update this to the “final” version after the tests in SR1 have been completed in 2006

## Slide 3
Fixed Frequency Trigger Veto ( FFTV ) :
Permanently enabled on all SCT TIM-3Cs
Pixels have asked for the FFTV to be temporarily disabled on their one TIM-3C at CERN
Existing algorithm asserts veto, on average, about once per one day of running with random triggers, giving a net loss of 1 msec per day ( = preset duration for of each veto )
To fully tests this with sufficient statistics will need about a month of continuous run. This will be done early in 2006
NOTE : In the ‘run mode’, the veto does not stop triggers from CTP being passed by TIM to the RODs. Executive decision needs to be taken, on how to protect FE opto-modules, in case the CTP does not stop issuing ( repetitive ) triggers when the veto line is asserted by TIM

## Slide 4
ROD Racks and Crates – Hardware Installation :
The current schedule indicates a possible slot for the installation of available SCT ROD crates and other hardware in the four ROD racks in USA15 during the last 3 weeks of January 2006
During this period, it is also planned to install all available TTC equipment in the TTC Rack, and to install any TTC connecting cables between the ROD and TTC racks
The actual cable routing will be done by CERN ( Serguei Maliukov ) - if requested beforehand
All available SCT off-detector electronics ( RODs/BOCs/TIMs ) will be installed in USA15 - if all services ( power, cooling, etc. are finished on time )
UCL will participate in this ( mp, tjf, etc. ) as required ( together with Cambridge )

## Slide 5
Opto-cables and Opto-ribbons Management :
All hardware required for back-of-ROD-racks cable management ( conduits, brackets, panels, etc ) had been made at UCL and is now stored at CERN
As much as possible of this hardware will be installed in ROD racks in USA15 during the proposed January 2006 slot
The actual cabling-up and routing of all Opto-cables and Opto-ribbons will only be possible after all the Opto-cables have been laid in USA15 later in 2006
The routing and connecting of individual Opto-ribbons will be a time consuming and exacting operation, and will require some 2-3 weeks minimum continuous period
UCL will participate in this ( mp, tjf, mw, etc. ) as required ( together with Cambridge )

## Slide 6
Type II/III Cables Sample QA Inspection and Testing :
Currently it is proposed that a small sample ( 8-10 ) of each batch of Type II/III cables is sent from the manufacturers to CERN every 2-3 weeks and be tested there
It is proposed that UCL ( mp ) will undertake this at CERN
First sample of few cables is expected at CERN now…
If it does indeed turn up, mp will go to CERN tomorrow to test the cables with Pippa, Sandra and Pepe, and to find out what exactly is required for the future tests