## Slide 1: ATLAS-SCT TIM OVERVIEW
TTC ( Timing, Trigger and Control)
Interface
Module
clock: BC Bunch Crossing clock
fast command:
L1A Level-1 Accept
ECR Event Counter Resett
BCR Bunch Counter Reset
CAL Calibrate signal
FER Front End Reset
event ID:
L1ID 24-bit Level-1 trigger no.
BCID 12-bit Bunch Crossing no.
TTID 8-bit Trigger Type
The TIM transmits the clock, fast commands and event ID from the TTC system to the RODs. The clock is sent via the back-of-crate (BOC) optocard
The TIM passes the Busy from the RODs via a Busy module to the CTP in order to stop it sending triggers
The TIM can send stand-alone clock, fast commands and event ID to the RODs under control of the local processor
The TIM is configured by the local processor setting up its registers. They can be inspected by the local processor
Ref: http://www.hep.ucl.ac.uk/~jbl/SCT/TIM_overview.html
http://www.hep.ucl.ac.uk/atlas/sct/tim/TIM_essential_model.pdf
http://www.hep.ucl.ac.uk/atlas/sct/tim/TIM_context.pdf

## Slide 2: SCT TTC System
The SCT has been allocated 4 partitions, each capable of running independently
The TTCvi module receives global ATLAS Level-1 signals such as the LHC clock and Level-1 Accept triggers. It can be programmed to generate SCT specific signals like Front-End Reset and Calibrate, and to run stand-alone
With only two ROD crates per partition, we expect to use a TTC VME transmitter (TTCvx) module instead of a TTC transmitter crate
TTCex encoder/transmitter module delivers the optimum optical signal level
The ROD Busy signals are combined into a Busy signal per partition, and then into the SCT Busy to the CTP in order to stop it sending triggers. Note that a partition Busy signal is input to both the SCT Busy and the Local Trigger box.
Ref : http://www.hep.ucl.ac.uk/atlas/sct/tim/SCT_Partitions_TTC_Busy.pdf