## Slide 1: Tracker Upgrade Electronics, Readout and DAQ
Matt Warren

## Slide 2: ATLAS Event Data Flow
Events data a stored on-detector in pipelines waiting for trigger decision
Calo/Muon data is used directly by Level-1 trigger
A Level-1 Accept (L1A) is distributed to modules
Module send data from pipeline off-detector to ReadOut Drivers (RODs)
RODs assemble event fragments and forward to ReadOut Buffers (ROBs)

## Slide 3: The existing SCT
4000 individual modules
  12 ASICs per module (usually)
Each module has bi-dir optical link
  100m long
  data output
  clock/control input
Links connected to RODs
RODs build event fragments and send to ROBs
RODs receive Timing, Trigger and Control (TTC) signals and distribute to modules
Note: no fast path, no ‘early data’
ROD
ROB
Level-1
via TTC
Module

## Slide 4: An Upgraded Tracker Design
SuperModule
Module
SMC
MCC
Opto Package
Modules of 20 ASICs
ASICs managed by a Module Controller (MCC)
  Or 2 MCC
10 Modules grouped into a SuperModule
MCCs connect to a SuperModule Controller (SMC) at an end of unit
Bi-directional optical link off-detector next to SMC
  High bandwidth 5-10Gb
Hence single readout link services 400 ASICs
ASIC
I. Wilmut
I. Wilmut

## Slide 5: More on the module design
MCC(s) received data from each ASIC in sequence (token)
  May be in smaller subgroups (dotted red lines) – useful for track trigger readout
ASICs grouped by layer (no way to compare top and bottom here)
First time top and bottom data have any chance of being compared is via MCC-MCC
Sensor
MCC
MCC
A. Greenall

## Slide 6: Track Trigger Idea: Level Zero Accept
Muon/Calo Level-1 identifies Region of Interest (RoI)
  Cone/tower radiating from centre.
RoI mapped to affected modules/supermodules/RODs (fast)
Level Zero Trigger (LZA) sent to the affected modules only
LZA copies data from the pipeline earlier than a L1A
Data is returned as high-priority via MCC and SMC to ROD
  bypassing FIFOs etc.
Geometry means few modules on a supermodule will be in a given RoI
  lets assume 10% - so minimal impact on readout bandwidth
ROD forwards data to L1 Track Finder
  via a dedicated, fast link
OR
Special dedicated Trigger link on supermodule handles LZA and Data.

## Slide 7: LZA (2)
Snags:
RoI finder system must be FAST, or we need longer pipelines
  or both
  (or SLHC runs at 20MHz …)
Additional signal/command on ASIC
Pros:
Only 1 additional signal/command on ASIC!
I’m guessing mods to ASIC are quite small: - New command and command-decoder - A 4 bit LZID counter (like the L1ID) - A MUX for selecting which counter (LZID or L1ID) is sent with data - A data extract point added mid pipeline - MUX to select LZ data or L1 data

## Slide 8: DAQ Now
Current system connects Modules -> RODs -> ROBs via optic-fibre.
  Many fibres into the ROD, 1 out (sounds like an SMC!)
ROD is “hosted” in a VME crate
  Provides power
  Configuration bus (over backplane)
  BUT data flows in-the-front and out-the-back.
The ROB is a PC with PCI (ROBINs)
  Data is transferred of the PC bus now, but
  Can be transferred out from cards directly

## Slide 9: A future ATCA based DAQ
ATCA is a telecoms standard
Cards are communicate using an array of links provided by the backplane
  Like the fibres connecting RODs to ROBs
Backplanes have HUB slots
  Point-to-point links from all other slots
Global clock links, config links.
A ROD could talk to a ROB in the same crate
Further ATCA cards can host Mezzanines – miniRODs
  1 or 2 supermodules/miniROD

## Slide 10: The End