## Slide 1: Tracker Upgrade Electronics, Readout and DAQ ATLAS Upgrade Workshop, Nikhef 4 November 2008
Matt Warren

## Slide 2: ATLAS Event Data Flow
Events data a stored on-detector in pipelines waiting for trigger decision
Calo/Muon data is used directly by Level-1 trigger
A Level-1 Accept (L1A) is distributed to modules
Module send data from pipeline off-detector to ReadOut Drivers (RODs)
RODs assemble event fragments and forward to ReadOut Buffers (ROBs)

## Slide 3: The existing SCT
4000 individual modules
  12 ASICs per module (usually)
Each module has bi-dir optical link
  100m long (.5us)
  data output (2 fibres)
  clock/control input (1 fibre)
Links connected to RODs
RODs build event fragments and send to ROBs
RODs receive Timing, Trigger and Control (TTC) signals and distribute to modules
Note: no fast path, no ‘early data’
ROD
ROB
Level-1
via TTC
Module

## Slide 4: DAQ Now
Current system connects Modules -> RODs -> ROBs via optic-fibre.
  Many fibres into the ROD, 1 out (sounds like an SMC!)
ROD is “hosted” in a VME crate
  Provides power
  Configuration bus (over backplane)
  BUT data flows in-the-front and out-the-back.
The ROB is a PC with PCI (ROBINs)
  Data is transferred of the PC bus now, but
  Can be transferred out from cards directly

## Slide 5: An Upgraded Tracker Design
40 ASICs = 1 Module
  2 ‘fingers’ of 20
ASICs managed by a Module Controller (MCC)
  Or 2 MCCs
10 Modules grouped into a SuperModule
MCCs connect to a SuperModule Controller (SMC) at an end of unit (copper, LVDS)
SMC connect via bi-directional optical link off-detector
  High bandwidth 5-10Gb
Hence single readout link services 400 ASICs
SuperModule
Module
SMC
MCC
Opto Package
ASIC
I. Wilmut
I. Wilmut

## Slide 6: More on the module design
Layout in 2 ‘fingers’
  20 ASICs/finger
  10 per readout group
MCC(s) receives data from readout group serially
  Each ASIC in sequence
Smaller subgroups (dotted red lines) possible
  useful for track trigger segmentation
Top and bottom sides independent
Sensor
MCC
MCC
A. Greenall
20cm

## Slide 7: Track Trigger Options
Level 1.5:
  Feed earlier tracking to Level-2
Higher L1A rate
  Move the problem off detector
On-detector event-selection
  ASICs decide on a good event and ‘push’ out of the module
“Level 0” Trigger
  RoI identifies a subset of module that might contain tracks
  Pre-trigger reads these out first

## Slide 8: Level 1.5 + Higher Rate
Level 1.5 is a pre-processor for Level-2
Hardware track-finder
Helps with decision
No change to detector
Off-detector splits data to Level-1.5 hardware
  At Slink, or
  ROD inputs, or
  Custom ROD output

## Slide 9: Higher Rate L1A
Supposed ‘Simple’ solution
  Data is moved off-detector where it can be processed as needed
  Level 1.5 (+2 + HLT) performs MORE data reduction
  No need for track-trigger – easy !
NOT A SIMPLE SOLUTION
  2-10x more data, power
  Probably necessitates fiber optic links to each module
  More copper
  More opto-links
  More RODs

## Slide 10: On-detector Event Selection
“Auto-trigger”
Use special trigger layers
  Attempt to keep as regular modules too
Cluster detection logic on ASIC, or
Co-incidence between layers
  No stereo angle
  Wafers spaced optimally for track finding
  ASICs span both sides of module
    Located at edge
    Flex-circuit
Needs track detection to be proven
Data needs to exit detector quickly***
ASIC
Wafer
Flex-circuit

## Slide 11: Level Zero Accept
Muon/Calo Level-1 identifies Region of Interest (RoI)
  Cone/tower radiating from centre.
RoI mapped to affected modules/supermodules/RODs
Level Zero Trigger (L0A) sent to the affected modules/regions only
L0A copies data from middle of pipeline
Data returned as high-priority via MCC and SMC to ROD
Geometry means few modules on a supermodule will be in a given RoI
  lets assume <10% - so minimal impact on readout bandwidth
Presume no need to cater for multiple triggers in readout window
  Fast-path buffer only 1 event deep
  If L0A ‘overlaps’ later events return “busy, no data”
ROD forwards data to L1 Track Finder
  via a dedicated, fast link, OR
Special dedicated Trigger link on supermodule handles L0A and Data.

## Slide 12: L0A L1/ASIC Integration
Needs more latency than in current system
  Longer pipelines required for ALL sub-detectors.
  ABC-N ASIC already has 255 deep
  Pixels already have 255
  Not heard of any show stoppers from other sub-dets either
Need fast path from module- problem (more later)
Additional logic on ASIC
  Secondary readout buffer
  FIFO leapover
L0A is much like our current L1A
  The new L1A happens later:
  2us for L0 (old L1, sortof) to identify features, issue L0A
  1us cable to detector (and back again)
  1us for us to readout
  2us for L1 decision. Issue L1A
  .5us cable to detector
  6.5us Total

## Slide 13: The Latency Problem
Tracker designed to readout at a sustained 100KHz
  ASICs in groups of 10
  Daisy chained together
  Serial readout at 80Mb
  80M/100k = 800 bits/chain/event = 80bits per chip/event
  So average latency is 10us. Needs to be 1us!
  If event readout in progress, need to wait, hence the 42 readout buffers.
L0 event can jump to head of readout queue
  Must still wait for current event to finish
  Unless it has a separate path link
Every ASIC adds header info
    2 bits header
    7 bits chip-address
    1 bit separator per hit
  >10% of data is overhead
Additional latency in MCC for packetising
E
M
Data
Token
MCC

## Slide 14: Latency ‘Solutions’
More loops
  Segment module for faster readout
Faster transmission
  Up the transmission speed from each
  320 MHz?
Bigger chips
  Increase the number of strips per chip
  320?
Protocol optimisation
  Can a fixed packet size work?
  Less headers
Point to point links to MCC
  Reduce protocol overhead – MCC knows chip address
SO:
Presuming event size is still 80b/128 strips = 200b/320 strips
  Rate is 320MHz*200 = .7us
  - Double for delay sending previous event, add MCC = 1.5us!!!
MCC

## Slide 15: Other problems
Level 0 processor will want synchronous in time with triggers
  Packetised data is a problem!

## Slide 16: Other options
Addional routing on PCB
Addional trigger link.