## Slide 1: Level Zero Accept
Muon/Calo Level-1 identifies Region of Interest (RoI)
  Cone/tower radiating from IP
RoI mapped to affected modules/supermodules/RODs
Level Zero Trigger (L0A) targeted at individual modules
Module copies data from middle of pipeline
Data returned as high-priority (queue jump) via MCC and SMC to ROD
Geometry means few modules on a supermodule will be in a RoI
  Assume <10% - so minimal impact on readout bandwidth
Presume no need to cater for multiple triggers in readout window
  Fast-path buffer only 1 event deep
  If L0A ‘pileup’ causes later events to return “busy, no data”
ROD forwards data to L1 Track Finder
  via a dedicated, fast link

## Slide 2: L0A Level-1/ASIC Integration
Needs more latency than in current system
  Longer pipelines required for ALL sub-detectors.
  ABC-N ASIC already has 256 deep
  Pixels already have 256
  Not heard of any show stoppers from other sub-dets either
Need fast path from module – difficult
Additional logic on ASIC
  Secondary readout buffer
L0A is much like our current L1A, new L1A happens later:
2.0μs | Level-0 (current Level-1...) identifies features. Maps to modules. Issues L0A
1.0μs | Cable to detector (and back again)
1.0μs | Level-0 event readout from tracker
2.0μs | Level-1 decision. Issue L1A
0.5μs | Cable to detector
6.5μs | Total

## Slide 3: The Latency Problem
Tracker designed to readout at a sustained 100KHz
  ASICs in groups of 10
  Daisy chained together
  Serial readout at 80Mb
  80M/100k = 800 bits/chain/event = 80bits per chip/event
  So average latency is 10μs. Needs to be 1μs MAX!
  If event readout in progress, need to wait (hence the 42 readout buffers)
L0 event can jump to head of readout queue, but
  Must wait for current event to finish
Every ASIC adds header info
  headers, chip-address, event ids, >10% of data is overhead
Must fit into MCC-SMC link
L1 wants data synchronous to L0A (fixed latency)
E
M
Data
Token
MCC
SMC

## Slide 4: Latency ‘Solutions’
Faster serial transmission - 160Mb?
  160Mb ASIC to MCC, requires 320Mb MMC to SMC
Bigger ASICs - Strips increased – 256?
  Less protocol overhead
Protocol/data-reduction optimisation - (event << 40bits?)
  Limit hits (1,2,3,many)
  Fixed packet size – decreased header/separator overhead
  L1ID, BCID counting on MCC?
  Packet split/abort – L0 packet transmitted mid L1 packet
No (or short) daisy-chains – reduces overhead
  No (or shorter) chip ID
  Easier event synchronisation
[The MMC-SMC link is the bottleneck, all the above is to reduce event size, with the largest contributution being a reduction in hits reported – we need to understand how little we can get away with – much simulation required (does 1,2, many work?) ]
Practical example (see diag) – minimal changes:
“Star” topology hybrid – direct ASIC-MCC connection
Event size fixed at 40bits
10 chips, 128 strips/chip, readout 80Mb
Data/event = 10*40=400. Latency thru MCC = 80bit event/80Mb rate = 1.0μs
MCC
SMC

## Slide 5: Conclusion (Help!)
Not easy!
Latency seems the biggest problem
  Need to reduce event size
Easy to write a talk, but we need the expert input:
  What are the hard limits?
  What can we work in?
  What can we get into the design now (without waiting for a rock-solid physics case)