## Slide 1: TIM Ticks
VME Interface (D32 tested, but not needed)
Clocks - Jitter, Fail-over
Backplane - Fast Signals, Serial IDs
TTC Interface - TTCrq, TTCrm
Stand-alone Signals - Internal, Front-panel NIM
Tested in the field - Cambridge, CTB, MDT (Nikhef)
16 TIMs Ready - Enough for SCT/Pixel needs
  Do not foresee any problems with remaining TIMs.
Firmware - Ready for shipping with board

## Slide 2: TIM Crosses
No TTCrq’s
  awaiting production version from CERN
Not fully tested TTC->(DAQ)->ROD flow
  In hand: ROD is at UCL, SBC is now booting, TDAQ is being installed, Alan is working on software.
‘New’ TIM functions (additional to original requirements):
Fixed Frequency Veto
  vetoing too many random triggers
  but work is still in progress
‘Busy Module’
  not clear if TIM has room for entire feature set
  may attempt to add these when needs become clearer

## Slide 3: Fixed-Frequency Veto Notes
Not performing as per TonyW’s Monte Carlo
  factor of >1000 worse!
  not clear if Monte Carlo or TIM is to blame (started reviewing source code <24 hours ago)
Have new diagnostic tools in firmware now
  Trigger-history FIFO logs period of EVERY trigger - but needs SBC for full 75kHz readout
  Various counters to log operation
A little more time and the problem should be understood 