## Slide 1
ATLAS SCT/Pixel TIM FDR/PRR
28 June 2004
Physics & Astronomy HEP Electronics
John Lane, Martin Postranecky, Matthew Warren
ATLAS - SCT TIM OVERVIEW

## Slide 2
TTC ( Timing, Trigger and Control)
Interface
Module
Clock: BC Bunch Crossing clock
Fast Commands:
L1A Level-1 Accept
ECR Event Counter Reset
BCR Bunch Counter Reset
CAL Calibrate signal
FER Front End Reset
Event ID:
L1ID 24-bit Level-1 trigger no.
BCID 12-bit Bunch Crossing no.
TTID 8-bit Trigger Type

## Slide 3: TIM CONTEXT
The TIM transmits the clock, fast commands and event ID from the TTC system to the RODs. The clock is sent via the back-of-crate (BOC) optocard
The TIM passes the Busy from the RODs via a Busy module to the CTP in order to stop it sending triggers
The TIM can send stand-alone clock, fast commands and event ID to the RODs under control of the local processor
The TIM is configured by the local processor setting up its registers. These can be inspected by the local processor
Ref : http://www.hep.ucl.ac.uk/~jbl/SCT/TIM_overview.html
http://www.hep.ucl.ac.uk/atlas/sct/tim/TIM_essential_model.pdf
http://www.hep.ucl.ac.uk/atlas/sct/tim/TIM_context.pdf
http://www.hep.ucl.ac.uk/atlas/sct/tim/TIM-1_LEB-2001_paper.pdf

## Slide 4
TTC Interface Module (TIM)
Backplane Drivers
Backplane Receiver
ROD Crate Controller
Registers
Configuration & Control
Read Out Drivers (RODs)
Clock
Fast Commands & Event ID
Busy
Read Out Drivers (RODs)
Standalone Clock + Control
Event ID FIFO
TTCrx
TTC System
Optical Signals
SCT TIM Essential Model
VME Slave Interface
HEP
MRMW/JBL v1.1 20-04-04
Sequencer
Busy OR, Mask & Monitor

## Slide 5
TTC Interface Module (TIM)
Event ID FIFO
TTCrx
VME Slave Interface
Standalone Clock & Control
Masked Busy OR
ROD Crate Controller
Registers
Configuration & Control
Timing Trigger & Control System
Optical Signals
Clock
Fast Commands & Event ID
Busy
Read-Out Drivers (RODs)
Busy Module
Timing & Control Logic
Read-Out Drivers (RODs)
Read-Out Drivers (RODs)
Global ATLAS Signals
ROD Crate Busys
SCT ROD Busy
Local SCT Control
SCT TIM Context
HEP
JBL/(MRMW) v2.0 20-04-04

## Slide 6: SCT TTC System
The SCT has been allocated 4 partitions, each capable of running independently
The TTCvi module receives global ATLAS Level-1 signals such as the LHC clock and Level-1 Accept triggers. It can be programmed to generate SCT specific signals like Front-End Reset and Calibrate, and to run stand-alone
With only two ROD crates per partition, we use TTC VME Transmitter (TTCvx) modules instead of a TTC transmitter crate
TTCex Encoder/Transmitter module delivers the optimum optical signal level
The ROD Busy signals are combined into a Busy signal per partition, and then into the SCT Busy to the CTP in order to stop it sending triggers. Note that a partition Busy signal is input to both the SCT Busy and the Local Trigger box.
Ref : http://www.hep.ucl.ac.uk/atlas/sct/tim/SCT_Partitions_TTC_Busy.pdf
http://ttc.web.cern.ch/TTC/intro.html

## Slide 7
4
3
2
TIM
CPU
RODs 1-8
RODs 9-16
TIM
CPU
RODs 1-8
RODs 9-16
RODs 9-16
TTCex 4
BUSY
TTCex 3
TTCex 2
TTCex 1
TTCvi 4
TTCvi 3
TTCvi 2
TTCvi 1
LTP 4
LTP 3
LTP 2
LTP 1
CPU
CTP Link
Local Trigger
Partition 1
Crate 1
Crate 2
Busy Partition 1
Busy
Global ATLAS Signals & SCT Busy
SCT Partitions of TTC and Busy
JBL/(MRMW) v2.0 20-04-04
HEP