## Slide 1
ATLA S SCT/Pixel TIM FDR/PRR
28 June 2004
Physics & Astronomy HEP Electronics
Martin Postranecky John Lane, Matthew Warren
TIM PCB LAYOUT

## Slide 2: TIM PCB
9U : 400 mm x 367mm
2.2 mm thick / 1.6mm edges
10 layers : 6x track
2x GND
2x Power
ECL and PECL clocks : Differential matched 100R impedance tracks of equal length
TTL clocks : split terminations
2x on-board vert. stiffeners
Rittal Front Panels and Injector/Extractor handles

## Slide 3: TIM-3A BOARD LAYOUT
VME Buffers
ROD Backplane Mapping & PECL Drivers
FPGA1 XC2S200E
(VME Interface)
NIM/ECL Signals I/O
TTCrm Module
J3 Backplane ROD Signals Output
TTC Fibre-optic Input
FPGA2 XC2S600E (TIM Functions)

## Slide 4: TOP SILK

## Slide 5: TOP PCB LAYER

## Slide 6: Temperatures :
1) Measured in ATLAS-SCT ROD crate, with fans at minimum speed, all TTC(n) commands running :
Ambient = +25 deg C
Fans temp = +28 deg C
All temp. sensitive labels on ICs and PCB below
+40 deg C
2) Measured outside crate on extender, with fans masked, all TTC(n) commands running:
Ambient = +25 deg C
All temp. sensitive labels on ICs and PCB below
+40 deg C