## Slide 1
ATLAS SCT/Pixel TIM FDR/PRR
28 June 2004
Physics & Astronomy HEP Electronics
Martin Postranecky John Lane, Matthew Warren
TTCrm versus TTCrq

## Slide 2: TTCrm
Originally selected as the TTCrx mezzanine board to be used on TIM-3
Uses 2 connectors J1 and J2
Just fits on single-width board
But last year reported :
Potential Phase Shift of the clock output of up to 400 ps, depending on the activity on the commands channel B
Potential increased clock jitter up to 150-200ps RMS on the TTCrm clock outputs

## Slide 3: TTCrq
Additional QPLL reduces this potential jitter from TTCrx chip to about 50 ps peak-to-peak
QPLL has narrow locking range of +/- 3.7 kHz around 40.0786 MHz ( < +/-100 ppm )
TTCrq board requires one additional connector J3 for the QPLL inputs/outputs ( in addition to the J1 & J2 )
7mm tall spacers on all connectors required for backward compatibility with TTCrm
Ref : http://ttc.web.cern.ch/TTC/TTCrqSpec.pdf
http://proj-qpll.web.cern.ch/proj-qpll/images/manualTTCrq.pdf
http://proj-qpll.web.cern.ch/proj-qpll/images/qpllManual.pdf

## Slide 4
A new mezzanine card is being designed as an alternative to the existing TTCrm supported by the CERN Electronics Pool (EP-ESS Group). The aim is twofold: to produce a card that can be mounted on a standard VME unit without imposing restrictions on the spacing between two modules and to add the QPLL functionality to the board1. Additionally the TrueLight pin-preamp (TRR-1B43-000) will replace the Agilent (HFBR – 2316).
The new TTCrx mezzanine card will be backward-compatible with the TTCrm. That means that the existing electrical connectors (J1 and J2) will be kept in the same physical positions with the same pinout. An additional connector (J3) will be added to the card located on the PCB side opposite to the optical connector side as represented in Figure 1. J3 will be a 26-pin connector. (VME board areas under the dotted/shadowed regions (top view drawing) should remain free for tool insertion during board removal.)
from the “TTCrx and QPLL Mezzanine Card ( TTCrq )”
        by Paulo Moreira, Ernest Murer
TTCrm versus TTCrq

## Slide 5: TTCrm versus TTCrq

## Slide 6: TTCrm versus TTCrq
TTCrm
TTCrq
J1 ( below ) J2 ( below )
J2 ( top ) J1 ( top )
J3 ( top )

## Slide 7: TTCrm CLOCK JITTER OBSERVED :
Up to 400 ps peak-to-peak on CLOCK40DES1 output pin J1 pin 2
Phase shift of clock seen when running with continuous L1A triggers
NOTE : Jitter on CLOCK40DES1 on J1 pin 2, triggering on the raising edge of clock, at about +1V trigger threshold, and about 10 usec ( = 400 clocks ) from trigger point
Scope set to infinite persistence

## Slide 8: TTCrm Clock Jitter
CLOCK40DES1
Trig. not running
200pS/div
Delay 10uS
Jitter ~ 400pS p-p

## Slide 9
TTCrm Clock Jitter
CLOCK40DES1
Trigger running
4.0nS/div
Delay 10uS
Clock Phase Shift

## Slide 10: TTCrm Clock Jitter
CLOCK40DES1
Trigger running
200pS/div
Delay 10uS
Jitter ~400pS p-p
Clock Phase Shift

## Slide 11: TTCrq CLOCK JITTER OBSERVED :
Up to 200 ps peak-to-peak on CLOCK40DES1 output pin ( with QPLL selected and locked )
When running with continuous L1A triggers, the QPLL looses lock repeatedly ( about once every 15 triggers received )
NOTE : The TTCrq module used in these tests was an untested sample on loan to UCL.
Our clock runs at 40.08 MHz, which should be inside the locking range

## Slide 12: TTCrq Clock Jitter
CLOCK40DES1
500pS/div
Delay 10uSec
Jitter ~ 200pS p-p

## Slide 13: TTCrq – Jitter on Backplane
PCLKB output
500pS/div
Delay = 10uSec
Jitter ~ 300pS p-p

## Slide 14: Clock Delay
CLOCK40DES1
PCLKB
Delay ~ 8nS

## Slide 15: CONCLUSION :
TIM-3B modified so that it will accept and run with either TTCrm or TTCrq.
All additional inputs and outputs on TTCrq connector J3 are connected to FPGA-2 to allow control and use of QPLL if required
Extra 7mm tall spacers required on all TTCrq connector pins for backward compatibility to TTCrm