## Slide 1
ATLAS SCT/Pixel TIM FDR/PRR
28 June 2004
Physics & Astronomy HEP Electronics
John Lane, Martin Postranecky, Matthew Warren
TTCrm versus TTCrq

## Slide 2: TTCrm
Originally selected as the TTCrx mezzanine board to be used on TIM-3
Uses 2 connectors J1 and J2
Just fits on single-width board
But last year reported :
Potential Phase Shift of the clock output of up to 400 ps, depending on the activity on the commands channel B
Potential increased clock jitter up to 150-200ps RMS on the TTCrm clock outputs

## Slide 3: TTCrq
Additional QPLL reduces this potential jitter from TTCrx chip to about 50 ps peak-to-peak
QPLL has narrow locking range of +/- 3.7 kHz around 40.0786 MHz ( < +/-100 ppm )
TTCrq board requires one additional connector J3 for the QPLL inputs/outputs ( in addition to the J1 & J2 )
7mm tall spacers on all connectors required for backward compatibility with TTCrm
Ref : http://ttc.web.cern.ch/TTC/TTCrqSpec.pdf
http://proj-qpll.web.cern.ch/proj-qpll/images/manualTTCrq.pdf

## Slide 4: TTCrm versus TTCrq
TTCrm
TTCrq
J1 ( below ) J2 ( below )
J2 ( top ) J1 ( top )
J3 ( top )

## Slide 5: TTCrm versus TTCrq

## Slide 6: TTCrm CLOCK JITTER OBSERVED :
Up to 400 ps peak-to-peak on CLOCK40DES1 output pin J1 pin 2
Phase shift of clock seen when running with continuous L1A triggers
NOTE : Jitter on CLOCK40DES1 on J1 pin 2, triggering on the raising edge of clock, at about +1V trigger threshold, and about 10 usec ( = 400 clocks ) from trigger point
Scope set to infinite persistence

## Slide 7: TTCrm Clock Jitter
CLOCK40DES1
Trig. not running
200pS/div
Delay 10uS
Jitter ~ 400pS p-p

## Slide 8
TTCrm Clock Jitter
CLOCK40DES1
Trigger running
4.0nS/div
Delay 10uS
Clock Phase Shift

## Slide 9: TTCrm Clock Jitter
CLOCK40DES1
Trigger running
200pS/div
Delay 10uS
Jitter ~400pS p-p
Clock Phase Shift

## Slide 10: TTCrq CLOCK JITTER OBSERVED :
Up to 200 ps peak-to-peak on CLOCK40DES1 output pin ( with QPLL selected and locked )
When running with continuous L1A triggers, the QPLL looses lock repeatedly ( about once every 15 triggers received )
NOTE : The TTCrq module used in these tests was an untested sample on loan to UCL.
Our clock runs at 40.08 MHz, which should be inside the locking range

## Slide 11: TTCrq Clock Jitter
CLOCK40DES1
500pS/div
Delay 10uSec
Jitter ~ 200pS p-p

## Slide 12: TTCrq – Jitter on Backplane
PCLKB output
500pS/div
Delay = 10uSec
Jitter ~ 300pS p-p

## Slide 13: Clock Delay
CLOCK40DES1
PCLKB
Delay ~ 8nS

## Slide 14: CONCLUSION :
TIM-3B modified so that it will accept and run with either TTCrm or TTCrq.
All additional inputs and outputs on TTCrq connector J3 are connected to FPGA-2 to allow control and use of QPLL if required
Extra 7mm tall spacers required on all TTCrq connector pins for backward compatibility to TTCrm