## Slide 1: TIM tests with ROD Crate
John Hill

## Slide 2: Test Setup
Readout facility at Cambridge with:
  Three detector modules on single pre-series SCT barrel harness
  Power from SCT prototype LV and HV cards
  Series ROD (Rev E) and BOC (Rev C) (transition card housing all incoming and outgoing fibre connections) with opto-plugins connected to harness fibre ribbons.
  TIM-3A
  CCT VP110 as SBC (current ATLAS standard CPU)
Purpose of tests are to confirm that TIM interface to ROD and BOC is working correctly.

## Slide 3
Module 2
Module 3
Module 1
6-way fibre ribbon
(Clock and Control)
12-way fibre ribbon
(Data)
LV/HV
Patch
Panel
Conventional
Electrical
Cables
Low-mass
Electrical
tapes
9U VME64x
crate
6U VME
crate
Schematic of layout for tests

## Slide 4: Simple tests
To confirm that the TIM/ROD interface is correct.
The following signals need checking:
  40MHz clock supplied to RODs from TIM. Clock is in fact supplied from TIM to BOC and then redistributed to the ROD.
  TTC signals from TIM to RODs. Eight signals (L1A,ECReset, BCReset, CAL, Serial ID, Serial TT, FEReset, spare) are supplied to each ROD.
  ROD BUSY from each ROD to TIM.

## Slide 5: Clocks

## Slide 6: TTC signals
Do the TTC signals propagate from TIM to ROD correctly?
L1A (TTC0) must be seen for triggering to occur at all.
ECR (TTC1) is counted in the top nibble of the L1ID, and synchronises the L1ID in the ROD and Front Ends.
BCR (TTC2) is required to synchronise the BC number in the ROD and Front Ends.
Serial ID (TTC4) – the ROD will not generate events until this is received, and the data must match that expected.
Serial TT (TTC5) – events should contain the Trigger Type as generated in the TIM.
FER (TTC6) and spare (TTC7) are not used by ROD – all we can do is look for signals on a scope.
CAL(TTC3) is not used in subsequent test – only employed when want to generate a calibrate pulse for the front ends.

## Slide 7: TTC signals
Background to this test:
  Setup ROD to accept triggers from TIM (rather than generated internally)
  Setup ROD and BOC in data-taking mode
  Setup TIM to generate triggers with correct BC offset (to allow for propagation time of commends to front ends).
  Generate a BCR to synchronise Bunch Count in ROD and front ends.
  Generate a ECR to synchronise Event Count. This also has effect of incrementing the ECR counter in the ROD (see the L1IDs reported).

## Slide 8
Loop setting Trigger Type to 1,2,4,…
and then generating a single TIM trigger
First event
L1ID=0x1000000
Last event
L1ID=0x1000007
Correct trigger type
Data due to
module in “send
mask” mode
ECR Count = 1
Decode first event

## Slide 9
No BCID or L1ID
errors
Decode last
event
Correct trigger type
(=27)

## Slide 10
again no BCID
or L1ID errors
(The other events were checked and were as expected)
These events indicate that TTC0-2, TTC4-TTC5 are transmitted correctly
and with the appropriate synchronisation.

## Slide 11: ROD BUSY
Three registers on TIM related to ROD BUSY:
  ROD BUSY – bit only set when BUSY present.
  ROD Latch – latches bit if BUSY present since cleared.
  ROD Monitor – latches bit if BUSY present for some time.
Test by resetting the ROD – this creates a busy signal for several seconds (there is no way to get the ROD to generate a BUSY by e.g. setting a register). Monitor the above registers at 100msec intervals.
Find that behave as expected – ROD BUSY only on when ROD BUSY set, other two registers latch.
All 16 ROD slots tested – correct bit set on each occasion (and the correct front panel LED on the TIM comes on). Necessary because the ROD BUSY line from each slot is on a separate backplane line.
ROD BUSY appears to be handled correctly by the TIM.

## Slide 12: Complex tests
Do TIM triggers produce the same results as triggers generated internally in the ROD?
To investigate this, do scans using both sorts of triggers and compare.