CLOCKING ISSUES WITH DAMC2 + CC RTM

1- The clock distribution/generation scheme under serious consideration.

The diagram below shows the scheme we are considering. The CC card refers to a combination of RTM and the base card.

TCLK (4.5MHz Bunch)
TCLK (99MHz FEE)
99MHz FEE
CLOCK GEN
XTCA BACKPLANE

2- Current capabilities of DAMC2
  - DAMC2 clock distribution circuitry consists of a I2C controlled XO and a 4x4 crosspoint switch.
  - XO can generate any-rate programmable frequencies from 10 MHz to 945 MHz and select frequencies up to 1.4 GHz. (according to the schematic part 10-810 MHz)
  - The start-up frequency for the part is 118 MHz. (according to the schematic part)
  - The crosspoint switch can route any of the four inputs to any of the four outputs and also can act like a low jitter clock fan-out buffer.
  - The diagram below shows the clock distribution circuitry.

XO
X-POINT
SWITCH

FPGA CLK
FMC CLK
SFP CLK
RTM CLK
CLK1-FPGA
OSC CLK
TCLK2
TCLK1

3- Issues
- There doesn't seem to be a PLL on the DAMC2 card. We want to generate the 99 MHz clock from the 4.5 MHz bunch clock by an external PLL.
- The PLL can be on the RTM. However, this clock must go back to the DAMC2 card to be distributed across the backplane on a TCLK line.
- According to the diagram and the clock circuitry schematic for the DAMC2, there is no facility to supply a TCLK to the xTCA backplane. (TCLKs are inputs to the x-point switch)
- Any generated clock on the RTM can return back to the FPGA via the RTM connector. (There is one pair on the RTM connector that is routed to a GCLK input of the FPGA)

TCLK (4.5MHz Bunch)
TCLK (99MHz FEE)
99MHz FEE
CLOCK GEN/SWITCH
XTCA BACKPLANE
PLL

99MHz FEE
99MHz FEE
4.5MHz

Currently not possible on DAMC2?

Would this be better? Sorting out the skew between master and slave cards

Only a PLL or PLL+zero delay buffer/fanout?

4- Solutions and more issues ( very very rough/sketchy/incomplete/silly)

- As stated above PLL can be on the RTM. 99 MHz clock is generated here.
  - Needs to go back to DAMC2
  - In turn needs to be on TCLK line for the slave cards
    - DAMC2 doesn't seem to drive any TCLKs.
  - All the RTM lines apart from one clock pair go to the FPGA
    - FPGA will direct the 99MHz clock to the slaves? (act as buffer?)
  - The skew problem. All the 99MHz clocks that the FEEs see should not have any skews.
    - Not quite possible here.
    - No feedback to the PLL on the RTM for possible deskewing
  - What about the data for the slave cards?
    - Data (generated by the FPGA) will be on the MLVDS bus
    - Clock will be on the TCLK lines
    - Alignment should be fixed? (Goes back to skew on the 99Mhz and there will be different delays on the data for different slaves)

- DAMC2 should incorporate a mechanism to drive TCLKs
  - Is just this enough. How can it be done? Bi-directional buffers TCLK lines?
  - Should it also incorporate an external PLL?
    - No need to send the 4.5Mhz clock to the RTM

What about TR generating the 99 MHz clock? :-)