TELEGRAM DATA TRANSMITTER (debug/in development)

The telegram transmitter module accepts data/events from the timing receiver logic and transmits them with a 108 MHz clock in a source-synchronous way. In the interface between the timing receiver logic and the transmitter logic, there is an asynchronous FIFO which is read at 108 MHz. The data from the FIFO is read at one byte at a time. The serialising logic also works at 108 MHz. Two state machines control the FIFO read operation and the serialising operation at 108 MHz. The FIFO contents are sent as packets with each of them having a predefined 8-bit header. An 8-bit CRC word is appended to each packet. An idle pattern of x”5885” is sent by the transmitter between packets.

INPUTS:

WRITE_CLK : This is the clock for the writes to the asynchronous FIFO. Can be different from the 108 MHz.

WR_EN : Write enable signal for the FIFO writes.

WR_TYPE : The type of the data to be written. (Event or Data see table x).

WR_DATA : The data to be written (in case of an event write it's don't care).

CLK108 : 108 MHz transmit clock.

RESET : Reset for the transmit logic.

OUTPUTS:

TEL_DATA_OUT : Differential transmitted data output.

TEL_CLK_OUT : Differential transmit clock output.

WRITE DATA STRUCTURE:

The data to be transmitted comprises either events (start_train, daq_ready, end_train) or data (train_number, bunch_pattern). The logic differentiates between different events and data according to the WR_TYPE signal. The table below shows the WRITE_TYPE signals and the corresponding event or data.

WRITE_TYPE	EVENT/DATA
“00010000”	Start Train (event)
“00100000”	End Train (event)
“01000000”	DAQ Ready (event)
“00000001”	Train Number (data)
“00000010”	Bunch Pattern Number (data)

The packet structures for data and events are defined as below:
     Start Byte (x2C) + Write_Type + CRC (for events)
     Start Byte (x2C) + Write_Type + Data (32-bit) + CRC (for data)

EXAMPLE SIGNAL DIAGRAM

D1a
x01
D1c
D1d
E1
D1b
x10
wr_clk
wr_en
wr_data
wr_clk
wr_type

ATTACHED CODE

test_telegram.vhd : Telegram transmit module.
telegrm_receive.vhd : Telegram receive module (for test/debug preliminary)
crc_gen_pkg.vhd: Package for the CRC function
.ucf : Added as an example

RESTRICTIONS (to be completed)