## Slide 1: TB slice test f/w
Post TB and CC meeting discussion
RH and CY (green comments from today)
14.12.2011
Notes: How to edit the title slide
Upper area: Title of your talk, max. 2 rows of the defined size (55 pt)
Lower area (subtitle): Conference/meeting/workshop, location, date, your name and affiliation, max. 4 rows of the defined size (32 pt)
Change the partner logos or add others in the last row.

## Slide 2: Assumptions w.r.t. initial slice f/w
Statement / Assumptions – tell me if these are wrong
The ¼ Mpxl demonstrator board has 8 output links
  Could also do a loop back test, e.g. 4 in and 4 out
Can use links to write data to target IP addresses (port@host)
The f/w scope is single board, no multi board capability
  If needed this could be provided later using the hooks inserted
Configuration is performed using a libTB.so based on Tim’s for the FEM
Configuration is performed through the front panel RJ45 Ethernet
  To ease configuration all 4 FPGA can be address mapped together
  The port@host send target list also need to have the corresponding MAC address specified of the host
The control (start, monitor, stop) s/w is based on Tim’s FEM solution. The control program running on a PPC (or softcore) is the server, client is off-board.
How to test the system before the prototype demonstrator?

## Slide 3: What we want to do – top down 
Do simple runs
Configure > start > monitor > stop
How many links are sending (involved) in a run?
Any number from 1 to 8 = the active set of links, called the set from now on
What types of data can be sent by a link?
Video pattern data (TYPE… the properties available are assumed to be defined by the f/w implementation)
Download data (data is opaque to f/w, only properties: length (the start address is defined by f/w implementation as is the maximum length)
It is possible to send different data types on different links

## Slide 4: Link and link set configuration
Link specific configuration:
Data type to send (Pattern or Download) and related properties
  Counted data (what is the definition) can also be injected
  Injection points will be listed by Rob.
The target address (port@host) list of ≥ 1entries to send data to
Mille second delay before next send in cycle
Possibly channel ON or OFF w.r.t. sending data (set membership flag), see below
Read configuration might be needed if loop backs are allowed
Link set send scheduling
Individual link start sending is chained. When a START command is received the first send on the first link in the set is sent and when the delay before the next send expires the send on the second link in the set is sent… this pattern propagates through all the links of the set… when the last link in the sets delay expires sending returns to the first link in the set… and continue until the CYCLE
Set configuration:
Links in set (see last comment in link specific configuration above)
CYCLE count
When a set and its links are configured we have a run configuration (see link in set comment)

## Slide 5: Commands need
Commands
START – starts the run configuration (toggle bit)
GET_STATUS – returns the status of the run (e.g. all local link counters including those not in set (i.e. ON))
STOP – stops the running run configuration (toggle bit)
  Would stop run when? After current link or current set?
RESET – clears all status counters
  Should be global, but could be link specific

## Slide 6: Example: two link set
Connect to demonstrator control server
STOP any ongoing run
Configure link 3
  set DATA_TYPE = PATTERN
  set FRAME_SIZE = 10000
  set FRAME_COUNT = 10
  set DELAY = 100
  set TARGET_LIST = port@host port@host port@host and corresponding host NIC MAC address
Configure link 5
  set DATA_TYPE = DOWNLOAD
  download NBYTES of opaque data
  set FRAME_SIZE = NBYTES
  set FRAME_COUNT = 1
  set DELAY = 50
  set TARGET_LIST = port@host port@host port@host
Configure link set
  set LINK_LIST = 3 5 (this would be obsolete if set ON was implemented at the link level)
  set CYCLE_COUNT = 10
START the run
GET_STATUS

## Slide 7: Observations
Additional properties: CRC creation on/off…?
A run that is not completely configured should generate an error, or is this a client side problem.
What is the content of the status counters?