## Slide 1: ZEUS MVD Helix Driver
VME wire-wrap board constructed.
  Contains registers that can be loaded via VME.
  Registers contain the HELIX setup data.
  Single VME cycle operation achieved by base address offset decoding in parallel with data transfer.
  Details at: http://www.hep.ucl.ac.uk/~dah/zeus/helix_driver_registers.html
  Setup data can be loaded into the registers and readback to check integrity.
  CLOCK, TRIGGER, NOT RESET, and TEST PULSE input from the MASTER.
  Output (LVDS to CAB) SERIAL DATA and LOAD pulse in addition to TRIGGER, RESET, TEST PULSE, and CLOCK.
  Status 13 January 2000: operational.
DAH/13Jan00

## Slide 2: Helix Driver
Mach5 CPLD implements VME interface and board logic.
A24:D16 VME interface.
LVDS -> TTL.
TTL -> LVDS.
Also TTL -> ECL for use with existing test setup.
DAH/13Jan00